## Slide 1
Statics
Balsa Wood Bridge Analysis and Testing
LabRat Scientific
© 2018

## Slide 2
This lesson is intended to be used in conjunction with the “Method of Joints” Classroom Lesson and the companion LabRat bridge test experiment video.

## Slide 3
2.0 Lbs
Bridge Analysis and Load Test
A simple dual-truss bridge will be built out of square balsa wood sticks and will be loaded to failure. A sample “Method of Joints” analysis will be completed for the loading case below:
11 inches
45⁰
45⁰
45⁰
45⁰
90⁰
90⁰

## Slide 4
The following sign conventions and nomenclature will be used in the analyses.

## Slide 5
Method of Joints – Force Sign Convention
Y
X
Positive X-Force Direction ( + F )
Negative X-Force Direction ( - F )
Positive Y-Force Direction ( + F)
Negative Y-Force Direction ( - F)
Recall: Forces are “vectors” and this show magnitude and direction.

## Slide 6
Force Notation - Examples
A
B
C
D
FAB
FBD
FAC
Positive Direction
Positive Direction
Negative Direction
The analyses will involve force variables and using this notation can help avoid confusion.
E
F
Negative Direction

## Slide 7
Method of Joints – Compression and Tension Convention
If the Force Vector is pointing towards the pin joint, then the member is in Compression.
If the Force Vector is pointing away from the pin joint, then the member is in Tension.

## Slide 8
Sin ϴ = Opp / Hyp
Cos ϴ = Adj / Hyp
Tan ϴ = Opp / Adj
Trigonometry Review
ϴ2
90⁰
Hyp
Opp = Hyp * Sin ϴ2
Adj = Hyp * Cos ϴ2
Opp2 + Adj2 = Hyp2
Forces will be assessed in the horizontal and vertical axes. As such, forces along a diagonal member will have to the broken down into their horizontal and vertical components.

## Slide 9
Generally speaking, truss problems are “static” in nature, which means nothing is moving. Under these circumstances any summed forces in the X-direction or Y-direction must add up to zero (no net force).
∑ Fy = 0
∑ Fx = 0
If there are no net forces acting on any point, Newton says that point will not experience any changes in its motion. Since we assume the points are initially at rest, this means the points will remain at rest…

## Slide 10
Load
1.0 Lb
1.0 Lb
Resulting Supporting Force
1.0 Lb
Resulting Supporting Force
1.0 Lb
System Free Body Diagram (FBD)
A
B
C
D
E
F
The first step is to determine the FBD for the entire system to identify reactive forces.

## Slide 11
Load
1.0 Lb
1.0 Lb
Resulting Supporting Force
1.0 Lb
Resulting Supporting Force
1.0 Lb
A
B
C
D
E
F
In this system FBD the upward forces are equal and opposite the downward forces. This means the system is in static equilibrium.

## Slide 12
We begin the Method of Joints analysis by selecting a joint (point) to start with. A Free Body Diagram for that point is developed and then the forces are analyzed.
You need to start with a joint that has at least one force defined.

## Slide 13
1.0 Lb
1.0 Lb
1.0 Lb
1.0 Lb
A
B
C
Free Body Diagram (FBD) of Point A on the bridge structure:
1.0 Lb
FAB
45⁰
45⁰
A
FAC
We want to calculate the forces in the two truss members that are joined at Point A. These forces are defined as FAB and FAC .
To do this, we set the sum the forces in the X-direction equal to zero and set the sum of the forces in the Y-direction to zero…

## Slide 14
1.0 Lb
The 1.0 lb supporting force is known from the system FBD.
Sum the Forces in the Y-direction ( ∑ Fy ):
∑ Fy = ( + 1.0 ) + ( - FAB * Sin (45) ) = 0
- FAB * Sin (45)
FAB
45⁰
45⁰
45⁰
45⁰
∑ Fy = ( + 1.0 ) + ( - FAB * 0.707 ) = 0
+ 1.0 = FAB * 0.707
FAB = 1.41 lbs
The direction of the FAB force vector was assumed. Since the mathematics generated a positive (+) FAB the assumed direction was correct. Had the result been negative we would have had to reverse the direction of the FAB arrow…
A
Analysis of Point A
FAB = + 1.0 / 0.707

## Slide 15
Now we need to assess the horizontal (X-direction) forces:
Sum the Forces in the X-direction ( ∑ FX )
∑ Fx = ( - FAC ) + ( - FAB * Sin (45) ) = 0
- FAB * Sin (45)
FAB
45⁰
45⁰
∑ Fx = (- FAC ) + ( - FAB * 0.707 ) = 0
+ FAC = - FAB * 0.707
FAC = - 1.0 lbs
Since the sign for FAC is negative (-1.0 lbs), the assumed direction for FAC was incorrect. As such the force arrow for FAC in the diagram above needs to be flipped…
FAC
Analysis of Point A
A
+ FAC = - 1.41 * 0.707

## Slide 16
Now we need to assess the horizontal (X-direction) forces:
FAB
45⁰
45⁰
FAC
Analysis of Point A
A
- FAB * Sin (45)
Sum the Forces in the X-direction ( ∑ FX )
∑ Fx = ( - FAC ) + ( - FAB * Sin (45) ) = 0
∑ Fx = (- FAC ) + ( - FAB * 0.707 ) = 0
+ FAC = - FAB * 0.707
FAC = - 1.0 lbs
+ FAC = - 1.41 * 0.707
Since the sign for FAC is negative (-1.0 lbs), the assumed direction for FAC was incorrect. As such the force arrow for FAC in the diagram above needs to be flipped…

## Slide 17
1.0 Lb
FAB = 1.41 lb
FAC = 1.0 lb
Analysis of Point A
This is the force in Member AB. The direction of the arrow indicates this beam is in compression.
This is the force in Member AC. The direction of the arrow indicates this beam is in tension.
A member in compression could start to bend and eventually buckle if it is not strong enough to resist the force. This is a failure mode to look for during testing…
A

## Slide 18
1.0 Lb
1.0 Lb
1.0 Lb
1.0 Lb
A
B
C
D
Free Body Diagram (FBD) of Point B on the bridge structure:
We want to calculate the forces in the three truss members that are joined at Point B. We already calculated one of the forces (FAB). The other two forces are defined as FBC and FBD .
Once again we sum the forces…
FAB = 1.41 lb
FBD
45⁰
45⁰
45⁰
FBC
B

## Slide 19
FAB = 1.41 lb
Analysis of Point B
The negative sign indicates the assumed direction for the force in FBC is incorrect. The force arrow for FBC in the diagram above needs to be flipped…
45⁰
45⁰
45⁰
FBC
B
Knowing FAB the other forces on Point B can be determined by once again summing forces.
Sum the Forces in the Y-direction ( ∑ Fy ):
∑ Fy = ( + 1.41 * Sin (45) ) + ( + FBC * Sin (45) ) = 0
∑ Fy = ( + 1.0 ) + ( + FBC * 0.707 ) = 0
FBC * 0.707 = - 1.0
FBC = - 1.41 lbs
FBC * Sin (45)
∑ Fy = ( + FAB * Sin (45) ) + ( + FBC * Sin (45) ) = 0
FAB * Sin (45)

## Slide 20
FAB = 1.41 lb
Analysis of Point B
The negative sign indicates the assumed direction for the force in FBC is incorrect. The force arrow for FBC in the diagram above needs to be flipped…
45⁰
45⁰
45⁰
FBC
B
Knowing FAB the other forces on Point B can be determined by once again summing forces.
Sum the Forces in the Y-direction ( ∑ Fy ):
∑ Fy = ( + 1.41 * Sin (45) ) + ( + FBC * Sin (45) ) = 0
∑ Fy = ( + 1.0 ) + ( + FBC * 0.707 ) = 0
FBC = - 1.41 lbs
∑ Fy = ( + FAB * Sin (45) ) + ( + FBC * Sin (45) ) = 0
FAB * Sin (45)
FBC * Sin (45)
FBC * 0.707 = - 1.0

## Slide 21
FAB = 1.41 lb
FBD
Analysis of Point B
45⁰
45⁰
45⁰
FBC
B
Now the X-direction forces are summed. Notice that this equation involves three forces.
Sum the Forces in the X-direction ( ∑ Fx ):
∑ Fx = ( + 1.41 * Sin (45) ) + ( - 1.41 * Sin (45) ) + ( - FBD ) = 0
∑ Fx = ( + 1.0 ) + ( - 1.0 ) + ( - FBD ) = 0
FBD = 0
∑ Fx = ( + FAB * Sin (45) ) + ( - FBC * Sin (45) ) + ( - FBD ) = 0
This is an interesting result. Beam BD is not off-setting any forces in the structure…
FAB * Sin (45)
FBC * Sin (45)

## Slide 22
FAB = 1.41 lb
FBD = 0
45⁰
45⁰
FBC = 1.41 lb
B
Analysis of Point B
The analysis indicates that Beam BC is providing the necessary X-direction and Y-direction balancing forces required for static equilibrium.

## Slide 23
1.0 Lb
1.0 Lb
1.0 Lb
1.0 Lb
A
B
C
D
F
Free Body Diagram (FBD) of Point C on the bridge structure:
There are several members joined at Point C. We already know the forces in two of the members and we know there is an external force (-1.0 lb).
We sum forces once again to calculate the unknown forces FCD and FCF …
FBC = 1.41 lb
FAC = 1.0 lb
C
1.0 Lb
FCD
FCF
45⁰
45⁰

## Slide 24
Analysis of Point C
FBC = 1.41 lb
FCF
45⁰
FAC = 1.0 lb
C
45⁰
Several of the forces acting on Point C are known from the previous calculations. Once again we sum the forces…
Sum the Forces in the X-direction ( ∑ Fx ):
∑ Fx = ( - 1.41 * Sin (45) ) + ( + 1.0 ) + ( - FCF ) = 0
∑ Fx = ( - 1.0 ) + ( + 1.0 ) + ( - FCF ) = 0
FCF = 0
∑ Fx = ( - FBC * Sin (45) ) + ( + FAC ) + ( - FCF ) = 0
- FBC * Sin (45)

## Slide 25
Analysis of Point C
FBC = 1.41 lb
45⁰
C
1.0 Lb
FCD
45⁰
Sum the Forces in the Y-direction ( ∑ Fy ):
∑ Fy = ( + 1.41 * Sin (45) ) + ( - 1.0 ) + ( + FCD) = 0
∑ Fy = ( + 1.0 ) + ( - 1.0 ) + ( + FCD ) = 0
FCD = 0
∑ Fy = ( + FBC * Sin (45) ) + ( - 1.0 ) + ( + FCD ) = 0
FBC * Sin (45)

## Slide 26
Forces in the Members of the Test Bridge
A
B
C
D
FAB = 1.41 lbs
FBD = 0
FAC = 1.0 lbs
Tension
Compression
E
F
FCD = 0
FCB = 1.41 lbs
FCF = 0
Tension
These are the forces in the members when a 2.0 lb load is placed on top of Member CF. All of the member forces will increase as the load is increased. An analysis of the right-hand side of the truss will yield the same results.

## Slide 27
A
B
C
D
FAB = 1.41 lbs
FBD = 0
FAC = 1.0 lbs
Tension
Compression
E
F
FCD = 0
FCB = 1.41 lbs
FCF = 0
Tension
The analysis seems to indicate that Member CD and Member EF could be removed without reducing the strength of the truss. This can be tested…
This is not the case for Member BD and member CF since they are critical to the rigidity of the truss – even though they carry no loads…

## Slide 28
Bridge models can be built and tested to see if the vertical zero-force members have an effect on the strength of the structure.

## Slide 29
Bridge A (Plank)
Bridge B
Bridge C
Experimental Test Bridges

## Slide 30
Materials
1/8” square balsa wood sticks (36” long)
White Glue
Hobby Knife (sharp)
Paper (for making templates)
Vertical supports (2x4 segments to ensure trusses are parallel when joined
Load Test Rig (see side) – buckets, small tables, boxes could be used
Load Beam (2x2 segment or similar)
Load container
String
Load (sand, rocks, other…)
Scale (to measure the weigh of the load when bridge fails)

## Slide 31
Paper templates were made to help ensure the trusses were constructed (nearly) identical.
The outer members were assembled first and allowed to dry.
Bridge Construction

## Slide 32
Once the glue had dried, the internal diagonal members were added.
The two trusses had dried, the were attached to a vertical support so that cross members could be added to join the trusses together. It is important that the two trusses are vertical.
Bridge Construction

## Slide 33
One bridge was built with the vertical members at the center.
Bridge Construction
One bridge was built without the vertical members at the center.

## Slide 34
For the experiment, all of the trusses need to contain the same amount of material so a 1 to 1 comparison can be made. The two truss bridges were nearly identical in weight.
A flat plank bridge was built to demonstrate the value of the truss configuration. Sticks were used to make the plank. The number of sticks was dictated by the needed weight of the bridge.
Bridge Construction

## Slide 35
A load stand was created so the bridges could be tested in a controlled manner.
Small rocks were placed in the container to apply the load to the bridge. The bridges were tested to failure.
The container was hanging from a stiff 2x2 wood bar in an attempt to make sure no asymmetrical loads are applied to the bridges.
Load Test Rig

## Slide 36
H1 - The plank bridge should fail under the smallest load since it does
not take advantage of the truss structure.
Hypotheses
H2 - The two truss bridges should fail at nearly the same load since the
center vertical members were determined to carry no load.

## Slide 37
Bridge-A (Plank) underwent a significant amount of bending before it failed.
The load at failure was 8.0 lbs

## Slide 38
Bridge-B (Truss w/ vertical members) was very stiff and flexed very little upto the point of failure.
The load at failure was 12.6 lbs

## Slide 39
Bridge-C (Truss w/o vertical members) was not as stiff as Bridge-B. In this image it is apparent that the rear, upper horizontal member had developed a significant bow just prior to failure.
The load at failure was 10.6 lbs

## Slide 40
Bridge | Bridge Weight (lb) | Failure Load (lb) | Structural Ratio (load/weight)
A - Plank | 0.02 | 8.0 | 400
B - Truss w/ Vertical Members | 0.02 | 12.6 | 630
C - Truss w/o Vertical Members | 0.02 | 10.6 | 530
The bridge with the vertical members was the strongest and most efficient structure.

## Slide 41
Hypothesis 1
The truss structures could carry more load and thus were the more efficient structures.
Proven to be CORRECT.

## Slide 42
Hypothesis 2
The analysis is for a “perfect” structure where all angles are precise, the structure remains perfectly vertical, all joints have the same strength, and all members have the same strength. The actual models were not “perfect”.
As indicated in the summary of member loads, it was suggested that the zero-load members were necessary for structural integrity. As the bridges were loaded, small initial asymmetries caused off-ideal alignments and loading which ultimately caused the zero-load members to become loaded. The vertical members in Bridge-B kept the top horizontal members from flexing and allowed the structure to hold more load.
Proven to be INCORRECT.

## Slide 43
Actual structures, no matter how carefully they are built, are not going to be “perfect”.
Conclusions
Theoretical analyses are only as good as the assumptions made. The assumption that the actual structure will be ideal is not a sound assumption.
A truss structure will carry more load than a simple plank structure of the same weight and material.
In general, zero-load members are important to the structural integrity of a truss structure and thus should not be removed from the design.
Truss structures tend to be stiff and can fail with little warning.