## Slide 1
Electronics
Batteries
Practice Problems
LabRat Scientific
© 2018

## Slide 2
6.0 V
6.0 V
6.0 V
V
What is the total voltage of the battery depicted below?
These cells are connected in series, so the voltages are added:
V = 6.0 V + 6.0 V + 6.0 V = 18.0 V

## Slide 3
12.0 V
12.0 V
12.0 V
V
What is the total voltage of the battery depicted below?
These cells are connected in parallel, so the total voltage is simply the voltage of the individual cells:
V = 12.0 V

## Slide 4
3.0 V
3.0 V
3.0 V
V
What is the total voltage of the battery depicted below?
Parallel Cells, thus
V = 3.0 V
It’s not really smart to connect batteries like this… It’s just an example.
Series connection:
V = 3.0 V + 3.0 V = 6.0 V

## Slide 5
How long can the 4 Amp-Hour battery run the electric motor if the motor draws 20 amps?
Battery Capacity 4.0 Amp-Hr
Duration = ---------------------- = ---------------- = 0.2 Hr
Current Draw 20 Amps
0.2 Hr = 12 min
M

## Slide 6
Is this a good idea?
No, batteries of different voltages should not be connected together.