## Slide 1
Electronics
Resistance
Practice Problems
LabRat Scientific
© 2018
R

## Slide 2
Band Color 1st Digit 2nd Digit Multiplier
Black 0 0 x 1
Brown 1 1 x 10
Red 2 2 x 100
Orange 3 3 x 1K
Yellow 4 4 x 10K
Green 5 5 x 100K
Blue 6 6 x 1M
Purple 7 7
Silver 8 8
White 9 9
Resistor Color Coding
Small resistors have colored bands around them. These bands identify the resistance of the resistor. The first two bands identify the numerical value of the resistor and the third band identifies the multiplier.

## Slide 3
Identify the resistance values for each of the resistors
Red = 2
Green = 5
Red = x 100
2,500 Ohms
Brown = 1
Black = 0
Yellow = x 10K = x 10,000
100,000 Ohms
Blue = 6
Blue = 6
Green = x 100K = 100,000
6,600,000 Ohms

## Slide 4
R1
R2
R1 = 500 Ohms
R2 = 2,000 Ohms
RTotal = 500 Ohms + 2,000 Ohms = 2,500 Ohms
Calculate the total resistance for the resistor network shown below.

## Slide 5
R1 = 3,000 Ohms
R2 = 3,000 Ohms
R1
R2
1 1 1 1 1 2
----- = ------ + ------ = --------------- + -------------- = ---------------
Rt R1 R2 3,000 Ohm 3,000 Ohm 3,000 Ohm
1 2
----- = --------------- = 0.00067 But we need to invert to get Rt = 1,492 Ohms
Rt 3,000 Ohm
Calculate the total resistance for the resistor network shown below.

## Slide 6
1000 Ohm
3000 Ohm
1000 Ohm
3000 Ohm
Calculate the total resistance for the resistor network shown below.
First step is to calculate the resistance for the parallel resistors
1 1 1 1 1 3 1
----- = ------ + ------ = --------------- + -------------- = --------------- + --------------
Rt R1 R2 1,000 Ohm 3,000 Ohm 3,000 Ohm 3,000 Ohm
1 4
----- = --------------- = 0.00133 But we need to invert to get Rt = 752 Ohms
Rt 3000 Ohm

## Slide 7
1000 Ohm
3000 Ohm
752 Ohm
The system now looks like the following series configuration:
Finally, the total resistance for the series network can be calculated:
RTotal = 1,000 Ohms + 3,000 Ohms + 752 Ohms = 4,752 Ohms