## Slide 1
Renewable Energy
Hydroelectric – Part 1
(Design)
LabRat Scientific
© 2019

## Slide 2
This lesson provides testing and engineering insights for developing a crude, home-built, hydroelectric generator using a Permanent Magnet Alternator (PMA), associated electrical components, and a wooden water wheel.
This lesson utilizes an experimental test set up for making torque and speed measurements that are used to design an appropriately sized water wheel to drive the system. The water wheel construction and testing are addressed in Part 2 of this educational series.

## Slide 3
SAFETY WARNING:
The components outlined in this lesson can be hazardous. The chains and sprockets pose a severe pinch hazard. Electrical components can generate excessive heat and high voltages that can cause injury. Appropriate safety precautions and supervision are required to conduct the experiments in a safe manner.

## Slide 4
Experimental Hardware
The bike peddles are cranked manually. The bike chain spins the bike wheel. The bike wheel is coupled to the alternator via a V-belt.
This rig was developed to study mechanical load requirements and associated electrical system performance in order to design a water driven power system.

## Slide 5
Experimental Hardware
Pulley Ratio = 1.76 / 0.22 = 8.0
Permanent Magnet Alternator
V-Belt
Bicycle Wheel
The “pulley ratio” can also be calculated just by using the radii… For every rotation of the big wheel, the alternator pulley will spin 8 times.
Wheel Radius = 0.28 m
Circumference = Pi x D
= 3.1416 x 0.56 m
= 1.76 m
0.28 m
Pulley Radius = 0.035 m
Circumference = Pi x D
= 3.1416 x 0.07 m
= 0.22 m
0.035 m

## Slide 6
12 VDC Light Bulb
Alternator system powering a 12 VDC light bulb.
1 rev/sec
8 rev/sec

## Slide 7
Typically contained within the modern automobile alternator
Alternator
12V Battery
Charge Controller
Steady
12 V DC
Power
Inverter
115 VAC 60 Hz Power
AC
Voltage
Bridge Rectifier
DC
Voltage
12 V Regulator
Steady
12 V DC
CAUTION! - Electrical components can cause electrical shock and injury. Car batteries are capable of providing very high electrical currents that can cause severe injury. Proper safety practices and supervision are required!
Ideal Electrical Configuration

## Slide 8
Electrical Set-up
Volt Meter
Bridge Rectifier
Alternator
Batteries
Power Inverter
Charge Controller
DC-DC Converter

## Slide 9
Alternators are used in cars to generate voltage to recharge the car battery and run electrical systems.
Alternators generate an Alternating Current (AC).
A car alternator has internal circuits to convert the AC electricity into 12 VDC electricity to be used in the car circuits.
Alternators are better than generators because the generate voltage more efficiently.
This alternator has been converted to a Permanent Magnet Alternator (PMA). It does not require 12 V to energize an internal electromagnet coil.
Permanent Magnet Alternator (PMA)

## Slide 10
While a standard alternator can be used, the alternator used in these experiments uses permanent magnets instead of the standard electromagnetic coil – making it a Permanent Magnet Alternator (PMA). This eliminates the need for an external 12 VDC power source to energize the coil.
Standard alternators include an internal Bridge Rectifier to output a DC voltage. The PMA alternator has also been modified to output the “raw” 3-phase AC voltage. AC power can be transmitted over longer distances better than DC power. This is useful when it comes to wind turbines and water wheels because they are generally installed some distance from where the power is actually needed.
Permanent Magnet Alternator (PMA)

## Slide 11
The AC output of the PMA is connected to an external Bridge Rectifier which converts the voltage into Direct Current (DC). This device would be located near the location needing the power.
The AC voltage generated by the alternator, is a function of the rotational speed of the alternator. This in turn means the voltage output by the Bridge Rectifier is also speed dependent. A fast spinning alternator can generate more than 30 volts.
Bridge Rectifier

## Slide 12
A steady 12 VDC output is needed for battery charging and operating an inverter. This is done using a DC-DC converter which converts the high input voltage to a constant 12 VDC.
The “excess” voltage is dissipated as heat – hence the fins on the casing.
DC-DC Converter

## Slide 13
The Charge Controller is used to ensure the battery is not over charged. This protects the battery from damage.
Charge Controller

## Slide 14
The hydroelectric generator system described in this lesson cannot power AC devices directly. Instead the system is used to recharge a bank of batteries which is capable of providing the current needed to power larger electrical devices via the inverter.
In these experiments two lawn tractor batteries are being used. Ideally, “deep discharge” batteries should be used since they are designed to be “drained” down to low voltage without damage. Deep discharged batteries are typically used in vehicles that don’t have alternators such as pleasure boats and golf carts.
Batteries

## Slide 15
The Power Inverter converts the 12 VDC into 115 VAC at 60 Hertz. This allows the system to power AC devices such as light bulbs, power drills, microwave ovens, and electric fans.
A 700 Watt inverter was used in these experiments.
Power Inverter

## Slide 16
Mechanical energy needs to be generated in order to turn the alternator and generate the electricity.
The first step in designing a system is to determine how much torque is needed to operate the alternator under an electrical load.

## Slide 17
Determining the Torque Required to Drive the System
12 VDC Light Bulb
Bridge Rectifier
Alternator
0.035 m
A Pull Test was conducted on the alternator to determine the torque needed to get it to spin at the proper speed.
PULL
Load Cell
The cord was pulled at a speed that caused the bulb to illuminate brightly…
Note: The wheel is not connected to the alternator pulley in this test.

## Slide 18
Alternator Pull Test
25 N
(with electrical load)
NOTE: The force required depends on the speed of the pull. All pull tests were conducted at a speed near the expected operational speed.

## Slide 19
Alternator Pull Test Results
No Electrical Load:
TorqueRequired = Force x Radius
TorqueRequired = 17 N x 0.035 m = 0.6 Nm
Small Electrical Load:
TorqueRequired = Force x Radius
TorqueRequired = 25 N x 0.035 m = 0.9 Nm
17 N
25 N

## Slide 20
Determining the Torque Required to Drive the System
PULL
The torque required to spin the wheel (which then spins the alternator) was determined by pulling on the edge of the wheel with a load cell while it is connected to the alternator via the V-belt..
Load Cell
12 VDC Light Bulb
Bridge Rectifier
Alternator
0.28 m
Various tests were conducted with no electrical load connected to the alternator output and then with a 12 VDC light bulb connected.
Note: The wheel is connected to the alternator pulley in this test.

## Slide 21
25 N
Theoretical Wheel Torque needed to Rotate the Alternator
Force measured from alternator pull test (w/ electrical load)

## Slide 22
0.28 m
25 N
Ideally, if we pull on the edge of the wheel with 25 N, the alternator should spin at the desired speed. However, if there is friction in the system, the actual pull force may be higher...
25 N
The V-belt pulls on the alternator pulley.
Force measured from alternator pull test (w/ electrical load)
The ideal (theoretical) torque is calculated as follows:
Torque = Force x Distance
= 25 N x 0.28 m
= 7.0 Nm
Theoretical Wheel Torque needed to Rotate the Alternator

## Slide 23
32 N (with electrical load)
Wheel Pull Test (w/ electrical load)
NOTE: The force required depends on the speed of the pull. All pull tests were conducted at a speed near the expected operational speed.
Note: This force is greater than the theoretical 25 N.

## Slide 24
Wheel Pull Test Results
The actual pull-load on the bicycle wheel (32 N) was higher than that which was predicted by the pull test on the alternator alone (25N).
This means there must be mechanical resistance in the wheel and belt system.
32 N
12 VDC light bulb connected

## Slide 25
32 N
12 VDC light bulb connected
With 12VDC Electrical Load Connected:
TorqueRequired = Force x Radius
TorqueRequired = 32 N x 0.28 m = 9.0 Nm
Wheel Pull Test Results

## Slide 26
 | Torque (Nm)
Theoretical Torque | 7.0
Measured Torque | 9.0
Theoretical vs. Measured
Approximately 33% more torque is required to overcome belt and bearing friction that is present in the system.
This serves as a baseline design factor when designing a water wheel or wind turbine to spin the alternator. For an initial design, provide at least 33% more torque than is required to spin the alternator. Maybe more, maybe less depending on the relative complexity of the mechanical system.

## Slide 27
 | Torque (Nm)
Alternator – No Load | 0.6
Alternator – Loaded | 0.9
Wheel – No Load | 5.6
Wheel – Loaded | 9.0
Effect of Electrical Load
The test data indicates that as the electrical load increases, so does the torque needed to spin the system. Approximately 50% more torque is required even with a relatively small electrical load. This factor will tend to grow as electrical load increases. This must be taken into consideration when approximating the amount of torque that will be needed for a particular configuration.

## Slide 28
Rotation Rate needed for 12 VDC Output
An experiment was conducted to determine the wheel rotation rate needed to produce a steady 12 VDC output.
Using video data, 5 rotations of the large bike wheel were timed while the system was generating 12 VDC. The 5 rotations took ~12 seconds, resulting in a spin rate of 0.42 Revolutions per Second (RPS).
Applying the 8:1 pulley ratio determined earlier, the alternator was spinning at 3.3 RPS.

## Slide 29
It’s not practical to manually spin the alternator by hand (or foot). It takes a fairly long time to re-charge the batteries and thus some sort of continuously operating system is needed to provide the rotational energy. This can be done in several ways, including wind power and water power.
Generating the Necessary Mechanical Energy
This lesson outlines how to spin the alternator using water power. A simple top-fed water wheel will be designed to meet the mechanical energy needs of the system.

## Slide 30
1.0 m Diameter Water Wheel
10 cm
Examining the geometry of the wheel configuration indicates that that 5 compartments will contain of water at any given time.
Water will enter the wheel at the top.
Water will spill out as the wheel rotates approximately 100 degrees.

## Slide 31
21 cm
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0.5 m
0.25 m
Water Wheel Geometry
Experimental Water Wheel:
15 Water Compartments
1.0 m diameter side disks made from plywood
18.4 cm (7.25”) wide 1.9 cm (¾”) thick wood planks to create compartments
Seams sealed with caulk
Note: The 1.0 m diameter was somewhat arbitrarily selected to ensure the wheel would have a good chance of working…

## Slide 32
Water Volume1 = ½ x 0.25 m x 0.1 m x 0.185 m = 0.0023 m3
1
2
3
4
5
Water Weight1 = Density x Volume
= 9800 N/m3 x 0.0023 m3
= 22.7 N
For estimating purposes, it is assumed that the weight of water is the same in compartments 1, 2, 3, and 4. The weight of water in compartment 5 is estimated to be 50% of the others.
Approximating the Weight of Water in each Compartment

## Slide 33
A digital load cell was used to verify that the assume “water cell” volume actually weighed the calculated 22.7 N.
Note: The load cell value was oscillating around 22.7 N and it just so happened that 22.7 N was captured in the photo (the world usually isn’t this perfect…)
Verifying the Weight of the Water
1 Liter = 0.001 m3
1 Liter
0.0023 m3 x -------------- = 2.3 liters
0.001 m3
Weight of bucket was nulled out
2.3 L
of Water
Load Cell
Calculating the volume of water in Liters:

## Slide 34
1
2
3
4
5
Estimated Moment Arms:
Compartment 1 = 0.16 m
Compartment 2 = 0.25 m
Compartment 3 = 0.31 m
Compartment 4 = 0.33 m
Compartment 5 = 0.24 m
Approximating the Moment Arms for each Water Compartment
Since gravity is providing the force to rotate the wheel, the moment arm used is the horizontal distance from the axis of rotation to the Center of Gravity (CG) of each cell of water.

## Slide 35
TorqueSupplied = (22.7 N x 0.16 m) + (22.7 N x 0.25 m) + (22.7 N x 0.31 m) + (22.7 N x 0.33 m) + (11.4 N x 0. 24 m)
Calculating the Supplied Torque
The total torque generated by the water wheel is the sum of the torques generated by each compartment containing water. The total torque is calculated as follows:
TorqueSupplied = (3.6 Nm) + (5.7 Nm) + (7.0 Nm) + (7.5 Nm) + (2.7 Nm)
TorqueSupplied = (26.5 Nm)

## Slide 36
 | TORQUE (N*m)
Required (loaded) | 9.0
Supplied | 26.5
From the calculations on the previous slide, a 1.0 m diameter, 0.2 m wide, 15 cell water wheel will provide approximately 3x the torque needed to spin the alternator (with a small electrical load).
This excess torque is important due to the fact that as the electrical load increases (i.e. more light bulbs), the torque requirement will increase. There will also be mechanical losses due to friction in the mechanisms (bearings, belts, etc.) that will reduce the “effective torque” in the system.
Calculating the Applied Torque

## Slide 37
Estimating Rotational Speed of the Water Wheel
The rotational speed of the water wheel will depend on several factors:
As shown in a previous slide, experiments indicate that a minimum rotational speed of 0.42 rev/sec (2.63 Radians/sec) is needed to achieve a steady state 12.1 VDC output.
The torque provided by the volume of water in the compartments (generated moment)
The rate at which water fills the compartments (how much water is deposited in the compartments in a given time)
The electromechanical resistive forces acting on the wheel. Electromechanical resistive forces include general bearing friction and belt friction as well as the resistive force caused by the alternator and the electrical load.

## Slide 38
Effect of Water Flow Rate
The rate at which water flows into the water wheel compartments will have an effect on the speed of the wheel and the supplied torque. As the electrical load is increased more torque will be required. As a result, the wheel will slow down. As the wheel slows down, more water will enter each compartment in the water wheel increasing the torque to keep the system working. However, at some point the torque requirement may become too large and the compartments will overflow. At this point the wheel will stop turning because insufficient torque will be available.
Experiments must be conducted to get a feel for how the performance of the water wheel will be affected by the water flow rate (Part 2 of this lesson).

## Slide 39
Overall System Efficiency
This indicates that the conversion of mechanical rotational power into electrical power is only about 10% efficient (Not good, but flowing water is free and continuous…)
PowerRotational = Torque (Nm) x Angular Velocity (Radian/sec)
P = Ƭ Ꙍ
P = 26.5 Nm x 2.63 Rad/sec (assume min rotational speed to get 12 VDC)
P = 69.9 Nm/sec = 69.9 Watts
PowerElectrical = Current (amps) x Voltage (voltage)
P = I V
P = 6.1 Watts (measured using power meter)

## Slide 40
Energy/Power Losses
Converting the alternator output to a DC voltage (via the Bridge Rectifier) involves electrical losses in the form of heat.
Converting the DC voltage to 120 VAC (via the inverter) also results in electrical losses in the form of heat.
Mechanical bearing and belt friction reduce efficiency.
The conversion of rotational energy into AC electrical energy in the alternator results in significant losses.

## Slide 41
Work is the area under the Torque-Rotation Angle curve
Work = ꭍ Ƭ dϴ
Work Done by the Water Wheel
Assuming a constant water source, the wheel will perform endless work since the Theta Angle (ϴ) is constantly increasing ( meaning ϴfinal --> ∞ ).
For constant Torque (Ƭ) Work becomes:
Work = Ƭ ( ϴfinal - ϴinitial )

## Slide 42
QUESTIONS ?