## Slide 1
Mathematics Concepts
Unit Analysis
LabRat Scientific
© 2018
1 Year
365 Days
-------------
1 Year
24 Hours
------------
1 Day
60 Minutes
---------------
Hour
60 Seconds
---------------
Minute

## Slide 2
Engineers and scientists deal with complex equations on a daily basis. In many cases several equations must be used in unison to solve an engineering or technical problem. If units are “mixed” (i.e. feet and inches), then incorrect answers will be generated.

## Slide 3
What is Unit Analysis?
Unit analysis is the process where the set of equations being used to solve a specific problem are looked at from a “unit” perspective to make sure they are compatible, and if unit conversions are necessary.
No numbers are used in these analyses. Once you know all the units are matched, then numbers can be used to get a quantitative solution.
This process is necessary because multiple equations may need to be combined to solve the problem, and if one equation involves “mass” and another involves “weight” for example, there will be an issue. Unit analysis would tell us that we will need convert the “weight” to “mass”, or visa-versa.

## Slide 4
The best way to understand the concept is to work through a few examples…

## Slide 5
Example 1 – Number of Seconds in a Year
1 Year = How many Seconds?
In this simple example we will work our way from “Year” to “Seconds”, by just looking at the units. Once we know we have the correct “equations” we can insert the necessary numerical values to answer the question…

## Slide 6
Example 1 – Number of Seconds in a Year
1 Year
In this simple example we will work our way from “Year” to “Seconds”, by just looking at the units. Once we know we have the correct “equations” we can insert the necessary numerical values to answer the question…
Days
--------
Year
First we look at how many days are in a year. The “Years” cancel…
Hours
--------
Day
Next, we look how many hours are in a day. The “Days” cancel…
Minutes
-----------
Hour
Next, we look at how many minutes are in an hour. The “Hours” cancel…
Seconds
----------- Minute
Finally, we look at how many seconds are in a minute. The “Minutes” cancel…

## Slide 7
Example 1 – Number of Seconds in a Year
1 Year
In this simple example we will work our way from “Year” to “Seconds”, by just looking at the units. Once we know we have the correct “equations” we can insert the necessary numerical values to answer the question…
Days
--------
Year
Hours
--------
Day
Minutes
-----------
Hour
Seconds
----------- Minute
We see that only “Seconds” are left after all the units are cancelled out, and this is the result we want. As such, we know that our assembly of conversions will give us the desired answer. Now we can put some values into the conversions and get the numerical answer to how many seconds are in a year.

## Slide 8
1 Year
365 Days
-------------
1 Year
24 Hours
------------
1 Day
60 Minutes
---------------
Hour
60 Seconds
---------------
Minute
1 Year = (365 * 24 * 60 * 60) seconds
= 31,536,000 Seconds
Inserting numerical values yields the following:
Because we performed the unit analysis, we are assured that we have not made some sort of mistake in a whether a “60” should be in the numerator or denominator, or whether we have omitted a needed conversion factor all together.
Example 1 – Number of Seconds in a Year

## Slide 9
Example 2 – The Drag Equation
The equation that governs aerodynamic drag is as follows:
Drag = ½ * Air Density * Velocity2 * Cd * Reference Area
In this example, we will assume a wind tunnel test was conducted with the goal to calculate the drag coefficient of the test article. The pertinent known units are as follows:
Drag = Newtons (N)
Reference Area = m2
Velocity = m/sec
Cd = a unitless coefficient
What units of Air Density should be used to make sure the calculations come out right?

## Slide 10
Example 2 – The Drag Equation
The first step is to rearrange the drag equation to solve for the desired parameter – in this case, Air Density.
2 * Drag
Air Density = -----------------------------------------------
Velocity2 * Cd * Reference Area
Next, we insert the units in to the equation.
2 * N
Air Density = ------------------------------
(m/sec)2 * Cd * m2

## Slide 11
N
Air Density = ----------------------
(m/sec)2 * m2
Example 2 – The Drag Equation
The “2” and the unitless “Cd” can be ignored since they don’t come into play in the unit analysis:
N
Air Density = ----------------------
m2
--------- * m2
Sec2
Next, rearrange the velocity squared term:

## Slide 12
Example 2 – The Drag Equation
Next, redistribute the “m” terms. This is a little bit tricky and requires the knowledge that density is a “mass per volume” term. This means we should establish the units for volume somewhere:
N
Air Density = ----------------------
m
--------- * m3
sec2

## Slide 13
Example 2 – The Drag Equation
Next, the trained eye should notice that the Weight (N) divided by an acceleration (m/sec2) is a mass (Kg).
N
Air Density = ----------------------
m
--------- * m3
sec2
Kg
= --------------
m3
And the end result is a mass per unit volume.
So, to get the drag equation to work out properly for our wind tunnel experiment, we are going to need to know the air density in Kg/m3.

## Slide 14
  ThrustMomentum = Mass Flow Rate x Exhaust Velocity
Rocket motors produce thrust by expelling mass with a certain amount of velocity. The equation that quantifies that thrust is as follows:
It is not intuitively obvious that the product of mass flow rate and exhaust velocity will generate the units associated with thrust (Pounds or Newtons). Unit Analysis can be used to make sure the units work out properly.
Example 3 - Momentum Thrust

## Slide 15
Let’s first look at “mass”, which is defined as the weight of an object divided by the acceleration due to gravity.
Lb
---------------
Ft
-----
Sec2
Weight
---------------
Accel
Mass =
=
Now, the “mass flow rate” is the amount of mass that passes some point (i.e. the throat of a rocket motor nozzle) every unit of time (sec). So, we should just be able to divide the mass equation shown above by time (seconds).
Example 3 - Momentum Thrust

## Slide 16
The first thing that needs to be done is to use some algebra to simplify the mass units. This is done by inverting the denominator (ft/sec2) and then moving it up into the numerator.
Lb
---------------
Ft
-----
Sec2
---------------
Sec
Mass
---------------
Time
Mass Flow Rate =
=
Example 3 - Momentum Thrust

## Slide 17
We also drop the outside parentheses since they no longer add any clarification.
Lb Sec2
--------- ---------
1 Ft
----------------------
Sec
Mass
---------------
Time
Mass Flow Rate =
=
Example 3 - Momentum Thrust

## Slide 18
Lb Sec2
--------- ---------
1 Ft
----------------------
Sec
Mass
---------------
Time
Mass Flow Rate =
=
Next, the terms in the numerator (BLUE) can be combined.
Example 3 - Momentum Thrust

## Slide 19
Next, the bottom denominator (RED) can be inverted then multiplied by the numerator.
Lb * Sec2
----------------
Ft
-------------------
Sec
Mass
---------------
Time
Mass Flow Rate =
=
Example 3 - Momentum Thrust

## Slide 20
Next, the seconds cancel out.
Lb * Sec2 1
------------- -------
Ft Sec
Mass
---------------
Time
Mass Flow Rate =
=
Example 3 - Momentum Thrust

## Slide 21
Lb * Sec2 1
------------- -------
Ft Sec
Mass
---------------
Time
Mass Flow Rate =
=
Example 3 - Momentum Thrust

## Slide 22
Lb * Sec
-------------
Ft
Mass
---------------
Time
Mass Flow Rate =
=
Example 3 - Momentum Thrust
This represents the simplified units for Mass Flow Rate…

## Slide 23
Lb * Sec Ft
------------- * -------
Ft Sec
Thrust = Mass Flow Rate * Velocity
=
Now that the “mass flow rate” has been simplified, the complete thrust equation can be considered:
It’s a simple case of canceling units. The “Ft” and “Sec” cancel out…
Example 3 - Momentum Thrust

## Slide 24
Lb * Sec Ft
------------- * -------
Ft Sec
Thrust = Mass Flow Rate * Velocity
=
Now that the “mass flow rate” has been simplified, the complete thrust equation can be considered:
It’s a simple case of canceling units. The “Ft” and “Sec” cancel out…
Example 3 - Momentum Thrust

## Slide 25
Lb Ft
------------- * -------
Ft
Thrust = Mass Flow Rate * Velocity
=
Now that the “mass flow rate” has been simplified, the complete thrust equation can be considered:
It’s a simple case of canceling units. The “Ft” and “Sec” cancel out…
Example 3 - Momentum Thrust

## Slide 26
Lb
Thrust = Mass Flow Rate * Velocity
=
Now that the “mass flow rate” has been simplified, the complete thrust equation can be considered:
All that is left is the units of pounds. And this is indeed the units for thrust.
Example 3 - Momentum Thrust

## Slide 27
Questions?