## Slide 1
Statics
Trusses and Load Analysis using Method of Joints
LabRat Scientific
© 2018
34⁰
1.0 lb
A
C
B

## Slide 2
Compression: The condition where loads work to squeeze an object together.
Tension: The condition where loads work to pull an object apart.
Torsion: The condition where external forces work to twist an object.
(while this action can affect a truss member it is not
addressed in this lesson)
Related Terms

## Slide 3
Structural Geometry
Rectangle: Does not resist lateral forces very well.
Triangle: Is a strong and ridged shape which resists loads well.
An examination of truss structures will reveal that triangles play a significant role in their design. The triangle is a very rigid and stable geometric shape:

## Slide 4
Structural Geometry
Compression
Tension
Bending
Rotation
Applied Force
Applied Force
When a lateral force is applied to a triangle it will retain its shape. If a lateral force is applied to the top of a square it will tend to deform.

## Slide 5
Notice all the triangles located throughout this bridge

## Slide 6
A truss is a structure made out of beams (a.k.a. members) whose purpose is to span a gap (i.e. a river). The truss supports the load and transfers it to points where is can be supported.
Structural Trusses

## Slide 7
Analyzing Loads in a Truss Structure
Two Methods:
  Method of Joints (focus of this lesson)
  Method of Sections
When designing a bridge, tower, or roof system engineers need to be able to calculate the magnitude of the forces acting on the truss members and whether the members are in tension or compression.

## Slide 8
The Method of Joints is used to calculate the forces acting on the pins or ball joints that join the truss members together. The joint forces then push/pull on the truss members which then push/pull on the other joints.
Method of Joints
When the analysis is complete all of the joint and member forces are known…

## Slide 9
Method of Joints – Force Sign Convention
Y
X
Positive X-Force Direction
Negative X-Force Direction
Positive Y-Force Direction
Negative Y-Force Direction

## Slide 10
Method of Joints – Compression and Tension Convention
If the Beam Force Vector is pointing towards the pin joint, then the beam is in Compression.
If the Beam Force Vector is pointing away from the pin joint, then the beam is in Tension.
The direction arrows are known as the “sense” of the force. The “sense” indicates whether the truss members are in compression or tension.
During the analysis we must initially assume the “sense” of the forces, but the mathematics will ultimately tell us if those assumptions were correct…

## Slide 11
Sin ϴ = Opp / Hyp
Cos ϴ = Adj / Hyp
Tan ϴ = Opp / Adj
Trigonometry Review
ϴ2
90⁰
Hyp
Opp = Sin ϴ2 / Hyp
Adj = Cos ϴ2 / Hyp
Opp2 + Adj2 = Hyp2

## Slide 12
Sample Problem – Simple Cantilevered Truss
34⁰
18 in.
15 in.
A
C
B
The Method of Joints can be used to analyze the pin and member forces in this simple cantilevered, triangular truss system.
The Method of Joints analyzes each connecting joint (A, B, and C) in the structure individually.
1.0 lb
An downward 1.0 lb external force is applied to the truss at Point A.

## Slide 13
Analysis for Point A
Free Body Diagram (FBD) for Point A.
1.0 lb
The 1.0 lb downward force is a given, so this makes Point A a good starting point for the analysis.
FAB
We know there is a diagonal member (AB) which must apply a force to Point A to keep it in static equilibrium. We label this force FAB and select its “sense”. We should realize this force needs to be pulling upwards to balance the 1.0 lb downward force…
FAC
We also know there is a horizontal member (AC) that is also applying a force to Point A. We label this force FAC but the “sense” is a little more difficult to determine. As such, we make our best guess…
A

## Slide 14
1.0 lb
FAC
34⁰
Analysis for Point A
Free Body Diagram (FBD) for Point A.
Since we have a known vertical force of 1.0 lb we should start off by analyzing the vertical forces (Y-direction). We will ignore the horizontal force for now…
FAB
Fup
There are two vertical forces acting on Point A – the downward force and the upward force being applied by Member AB.
We need to sum the forces in the Y-direction. Since the system is assumed to be in static equilibrium, the sum of the forces must be equal to zero.
∑Fy = 0
∑Fy = (+ Fup) + (- Fdown) = 0
The negative (-) sign indicates a downward force.

## Slide 15
Analysis for Point A
The problem is, we don’t know the magnitude of the upward force…
1.0 lb
FAC
34⁰
FAB
Fup
Fup = + Sin(34) * FAB
However, using trigonometry we can express this upward force in terms of the force in Member AB. This force is FAB .
+ Sin(34) * FAB
34⁰
We can apply a little algebra to determine the magnitude of FAB …
∑Fy = (+ Sin(34) * FAB) + (- 1 lb) = 0
Inserting the “forces” into the force equation yields:
∑Fy = (+ Fup) + (- Fdown) = 0

## Slide 16
Analysis for Point A
(+ Sin(34) * FAB) + (- 1 lb) = 0
1.0 lb
FAC
34⁰
FAB
Fup
+ Sin(34) * FAB
34⁰
(+ 0.56 FAB) = (+ 1 lb)
FAB = (+ 1 lb) / (0.56)
FAB is ultimately what we want since it tells us the magnitude of the force in Member AB.
Since the math used to generate FAB results in a positive (+) value for FAB the sense we selected is correct.
FAB = 1.8 lb

## Slide 17
Analysis for Point A
1.0 lb
34⁰
FAB = 1.8 lb
The next step is to analyze the horizontal (X-direction) forces at Point A.
FAC
In our original diagram we had already defined force FAC as being generated by the horizontal Member AC. We defined (guessed?) it as a left-pointing force so it is a negative (-) force.
The diagonal Member AB is also pulling on Point A. This force is the horizontal component of FAB. We already determined that FAB was pointing towards the right, so the component will also point towards the right. As such, it is a positive (+) force.

## Slide 18
Analysis for Point A
1.0 lb
FAC
34⁰
FAB = 1.8 lb
Inserting the forces into the force equation yields:
∑Fx = ( + Cos (34) * FAB ) + ( - FAC ) = 0
+ Cos (34) * FAB
( + Cos (34) * FAB ) = ( + FAC )
Performing some simple algebra yields:
( + .83 * 1.8 lbs ) = ( + FAC )
FAC = 1.5 lbs
As was done in the Y-direction, the X-direction forces are summed and set equal to zero.
∑Fx = 0

## Slide 19
Analysis for Point A
1.0 lb
FAC
34⁰
FAB = 1.8 lb
+ Cos (34) * FAB
FAC = 1.5 lbs
FAC is the force generated by the horizontal Member AC. Since the sign of FAC was calculated as a positive value (+ 1.5 lbs), the “left-ward sense” that was originally selected for FAC was correct…
Force FAC balances the right-ward force component being generated by the diagonal Member AB and thus keeps the system in static equilibrium in the X-direction.

## Slide 20
Analysis for Point A
1.0 lb
FAC
FAC = 1.5 lbs
Component of FAB = 1.5 lbs
Component of FAB = 1.0 lb
If we look at the X and Y forces acting on Point A we see that they all balance each other – indicating the system is in static equilibrium.

## Slide 21
34⁰
A
B
C
Forces in the Truss Members
FAB = 1.8 lb
FAC = 1.5 lb
By analyzing Point A we were able to determine the magnitude and correct sense of the forces in the two truss members…

## Slide 22
Compression and Tension State
From the vector convention defined earlier we can identify if the beams are in tension or compression.
We can use this information to design the members in the truss…
We now know the forces in the members, but we also need to know the reactive forces being generated by Point B and Point C…
34⁰
A
B
C
1.5 lb
1.8 lb
TENSION
COMPRESSION

## Slide 23
B
FAB = 1.9 lb
34⁰
Adj = Cos (34) * 1.8 = 1.5 lb
Opp = Sin (34) * 1.8 = 1.0 lb
Analysis for Point B
From the previous calculations we can conclude that Member AB exerts a diagonal force on Point B.
This force can be broken into horizontal and vertical components.

## Slide 24
Analysis for Point B
B
To find the reactive forces being generated by Point B to keep the system in equilibrium we simply sum forces in the X and Y directions and set them equal to zero as was done for Point A.
1.5 lb
1.0 lb
FBx = + 1.5 lb
FBy = + 1.0 lb
These are the forces being applied by Point B to resist the force being applied by Member AB.
∑Fx = ( FBx ) + ( - 1.5 ) = 0
FBx
∑Fy = (FBy) + (- 1.0 lb) = 0
FBy

## Slide 25
C
1.5 lb
FCx
Analysis for Point C
∑Fx = ( - FCx ) + ( + 1.5 ) = 0
FCx = + 1.5 lb
Horizontal force being applied by Member AC
This is the force being applied by Point C to resist the force being applied by Member AC.

## Slide 26
34⁰
A
B
C
1.5 lb
1.8 lb
TENSION
COMPRESSION
1.5 lb
1.5 lb
1.0 lb
1.0 lb
1.5 lb
The forces acting on the system

## Slide 27
But does the Method of Joints generate reliable results?
The simple truss model used in the analysis makes it fairly easy to conduct experiments to determine the actual compressive and tension forces in the truss members…

## Slide 28
Experimental Set-up
1.0 lb Test Weight
Digital Load Cell
Truss Structure
Force Measurement

## Slide 29
A force pushing into the load cell will produce a negative (-) force reading.
A force pulling on the load cell will produce a positive (+) force reading.
Digital Load Cell – Sign Convention

## Slide 30
An experiment was conducted to verify the theoretical calculation.
Digital Force Meter
1.0 lb Weight
The force in the horizontal member was measured to be -1.56 lbs. which is very close to the calculated theoretical value of 1.5 lbs. The negative sign on the force value displayed on the computer screen indicates the force is pushing towards the right. This is consistent with the direction determined in the analysis. This verifies that the horizontal member is under compression.
Experimental Verification

## Slide 31
Experimental Verification
A second experiment was conducted to measure the load in the diagonal beam.
In this experiment the digital force measuring device was attached the diagonal beam. The same 1.0 lb test weight was applied to the end of the truss.
The load in the diagonal member was measured to be +1.85 lbs which is very close to the calculated theoretical value of 1.8 lbs.

## Slide 32
The experimental results were in fairly good agreement with the theoretical calculations.
 | Theoretical | Experimental
Member AB | 1.8 lb | 1.85
Member AC | 1.5 lb | 1.56
Comparison of Results
The differences are well within the length and angle measurement errors.

## Slide 33
Building a Balsawood Truss Bridge
The Method of Joints can be used to analyze a balsa wood bridge (maybe you have a competition in engineering class…). While you may not be deeply concerned about the actual forces at the joints (since you probably won’t go as far as calculating the strength of your glue joints), it is pretty important to determine whether the various members are in compression or tension. In general, members that are in tension can be lighter than members in compression because the members that are in tension won’t have a buckling concern. This might allow you to build the lightest and strongest bridge…
See the companion balsa-bridge classroom lesson and testing video…

## Slide 34
Questions ?
34⁰
1.0 lb
A
C
B