## Slide 1: ROCKET DRAG
LabRat Scientific
© 2018

## Slide 2
What is Drag ?
Drag includes a “pressure” force and a “frictional” force
  High pressure when acting on the front of a moving object
  Low pressure (suction) at the back of a moving object
  Friction along the body of the object
Drag always acts to slow down the rocket
High Pressure
Low Pressure
High pressure pushes on the front of the rocket – tends to slow the rocket down.
Low pressure on the back of the rocket tries to suck the rocket backwards – tends to slow the rocket down.
Direction of Motion
Friction

## Slide 3
Getting a “Feel” for Drag

## Slide 4
The rocket disturbs the air as it moves through it. This disturbance is “drag”…

## Slide 5: The Drag Equation
Drag = ½ x Air Density x Velocity2 x CD x Reference Area
Air Density decreases as altitude increases (it’s variable…).
Velocity tends to be variable also. Drag is a function of the “square” of the velocity.
The Drag Coefficient (CD) is the “shape factor” that characterizes the drag nature of the object.
The reference area (usually the “body tube” area when viewed from the end) allows the drag to be scaled relative to the size of the object.

## Slide 6: The Impact of Drag…
Recall the expanded version of Newton’s Second Law of Motion…
Thrust - Drag - Weight
Accel = --------------------------------------
Mass
Acceleration becomes smaller (and maybe negative) as drag becomes larger
A lower acceleration translates into a lower velocity… Integrate a smaller acceleration and you get a smaller velocity…
A lower velocity means the rocket will not fly as high

## Slide 7
Increased Rocket Performance through Drag Reduction

## Slide 8
High Pressure
Low Pressure
Direction of Motion
Reduce High Pressure on Front by adding a Nose Cone
Less High Pressure
Low Pressure
Direction of Motion

## Slide 9
Better Configuration
A blunt nose will create a higher pressure force, and will cause the flow to separate at the forward end of the body tube, which creates more drag.
Nose Drag
While the long nose cone will have more surface area and thus more skin friction drag, the flow is much smoother around the front of the rocket, which reduces drag overall.

## Slide 10
Reduce Low Pressure on Aft End by adding a Boat Tail
High Pressure
Low Pressure
Direction of Motion
Large Area
High Pressure
Low Pressure
Direction of Motion
Smaller Area
Recall:
Pressure x Area = Force

## Slide 11
Better Configuration
Base Drag
The wide base of this rocket causes flow separation and high pressure drag at the back of the rocket.
Tapering the back of the rocket allows the flow to curve around more easily and reduces the size of the low pressure area behind the rocket. The tapered section is know as a “boat tail”, and they can be a little tricky to construct…

## Slide 12
Even with a boat tail, there is going to be base drag on the body tube.
Base Drag - Coasting

## Slide 13
The rocket’s drag is lower during motor burn since the rocket motor exhaust “reduces” the low pressure at the base of the rocket. Its sort of a perfect boat tail…
Base Drag - Thrusting

## Slide 14
Fin Drag
Better Configuration
Fins suffer the same issues as the rocket body – high pressure at the front, low pressure at the back, and friction
Fins need to have curved leading and trailing edges to reduce the total pressure drag.
The number of fins must be minimized as well. 3 or 4 fins are adequate to provide the necessary stability. More fins are just unnecessary drag producers…

## Slide 15
Poor paint job with bubbles and runs
Fins that are too large and not sanded smooth
Launch lug that is too big
Better Configuration
Make Your Rocket Smooth and Streamlined
Make fins only as large as they need to be for stability. Sand fins smooth and maybe sand “fuzz” off the body tube. Cover the rocket with a even coat of paint to give a smooth, slick finish.
Higher total drag

## Slide 16
Rough Rocket Skin
Smooth Rocket Skin = Less Drag
A turbulent flow interacts with the rocket skin more and thus creates more drag. Drag is reduced if the flow can be kept smooth…
Smooth Surface = More Laminar Flow = Less Drag

## Slide 17
Reduce Interference Drag
White glue can be used, but you can only effectively build up one fillet at a time…
Add Fillets to Make a Smooth Transition from Fin to Body Tube
The flow around the fins “interferes” with the flow along the body – and visa versa

## Slide 18
Calculation
of
Theoretical Model Rocket Drag

## Slide 19: The Drag Equation
Drag = ½ x Air Density x Velocity2 x CD x Reference Area
Recall the basic equation for calculating the drag force acting on the rocket:
The trick is to be able to estimate the drag coefficient (CD) of the rocket…

## Slide 20
The Total Drag Coefficient is derived by taking the sum of CD’s calculated for the various major elements of the rocket.
Total Drag Coefficient
CdSF = Skin Friction Drag Coefficient
CdB = Base Drag Coefficient
CdL = Launch Lug Drag Coefficient
CdI = Interference Drag Coefficient
+ CdB
+ CdI
+ CdL
CdTotal
= CdSF
If you design a rocket with all kinds of “stuff” handing off it, you will need to calculate the “stuff” drag coefficient. That can become very difficult.

## Slide 21
Determining the drag coefficient of a rocket is not a trivial task. There are a lot of equations and assumptions involved.
What a drag…

## Slide 22
The equations we are about to examine (or be confused by) were not conjured out of thin air, they were derived from countless wind tunnel tests during the 1930’s, 40’s and 50’s…
Somehow, smart people in the past devised mathematical equations that approximated the data that was collected in wind tunnels…

## Slide 23
Some Basic Rocket Geometry
ABT
d
L
ABT
a
d
c
a + b + c
Chord Ave = ------------
3
Tip Chord
Root Chord
ABT = Pi x (Body Radius)2
S wet, body = Pi * Body Diameter * Length (approx. since nose is not a cylinder)
S wet, fins = Fin Area * No. fins * 2

## Slide 24
Skin Friction Coefficient
This is the most difficult parameter to estimate. There are 3 equations that can be used, and the appropriate equation to be used depends on how the airflow is moving around the rocket.
Before we can estimate all the various CD values, we need to calculate one critical factor – The Skin Friction Coefficient…
The Skin Friction Coefficient depends on whether the airflow passing over the rocket skin is nice and smooth (laminar) or all mixed up (turbulent). The type of airflow is governed by the Reynolds Number (Re).
Before we get to Re, lets look at the equations…

## Slide 25
Critical Reynolds Number
Surface Roughness Height
Recritical = 51 * ----------------------------------------
Rocket Length
- 1.039
Surface | Roughness Height (in) | Roughness Height (m)
Rough Finish | 0.76 | 0.0197
Unfinished Surface | 0.23 | 0.0059
Regular Paint Finish | 0.094 | 0.0024
Smooth Paint Finish | 0.031 | 0.00079
The critical Reynolds Number gives us an idea where along the rocket the flow will trip from laminar (smooth) and turbulent (all mixed up). The closer to the nose the tripping point, the higher the drag…

## Slide 26
Density * Velocity * Rocket Length
Re = -----------------------------------------------------
Absolute Viscosity
Reynolds Number
ASSUMPTIONS:
Air Absolute Viscosity = 0.000012024 lb/(ft*sec)
Air Density = 0.076314 lb/ft3
Rocket Length = 3 ft
Velocity = 150 Ft/sec
Reynolds Number is unitless with a magnitude in the low millions…

## Slide 27
If Re < 100,000 Cf = 1.48 x 10 -2
1
If 100,000 < Re < Re critical Cf = ----------------------------
((1.5 * ln Re) - 5.6) 2
Skin Friction Coefficient
L = Length of rocket
Rs = Surface Roughness Height (make a guess based on the surface
of your rocket and the previous table)
ln = natural log
Rs 0.2
If Re > Re critical Cf = 0.032 * -------- L
We look at the rockets Reynolds Number relative to the rocket’s critical Reynolds number to determine what equation to use.

## Slide 28
Compressibility Corrections
Subsonic Cfc = Cf * ( 1 - (0.1 x M2) )
Cf
Supersonic Cfc = Cf * -------------------------------
(turbulent) ( 1 + (0.15 x M2) ) 0.58
The drag changes drastically when the flow becomes supersonic. This should be accounted for in “real rocket science”, but for typical model rockets that fly below the speed of sound, it’s not a real concern…

## Slide 29
Body & Fin Skin Friction Drag Coefficient
1 2 * t
(1 + ------- ) * S wet, body + (1 + ------ ) * S wet, fins
2 * fb c
CdF = Cfc * -----------------------------------------------------------------
A BT
S wet, body = Wetted surface area of body tube
S wet, fins = Wetted area of all fins, both sides (Fin Area x No. fins x 2)
A BT = Body tube reference area (area of the body tube when viewed from the end)
c = Average chord length
Cfc = Skin friction coefficient - corrected
fb = Fineness ratio of the rocket (rocket length / rocket diameter)
t = Fin thickness
Since this is a unitless coefficient it doesn’t matter what units are used, as long as they are consistent.

## Slide 30
0.029
CdB = --------------
Cfc
Base Drag Coefficient
Cfc = skin friction coefficient - corrected

## Slide 31
t CR
CdI = Cfc * ( 1 + 2 * --------- ) * ---------- * d * n
c Ave S wet body
CR = Fin Root Chord
cAve = Average Fin Chord
S wet body = Wetted Surface Area of Body Tube and Nose Cone
Cfc = Skin Friction Coefficient - corrected
d = Body Diameter
n = Number of Fins
T = Fin Thickness
Interference Drag Coefficient

## Slide 32
1.2 ALL + (0.0045 * S wet lug )
CdL = --------------------------------------
S wet body
Launch Lug Drag Coefficient
A LL = Cross-sectional Area of Launch Lug
S wet lug = Wetted Surface Area of Launch Lug
S wet body = Wetted Surface Area of Body Tube and Nose Cone

## Slide 33
Drag = ½ x Air Density x Velocity2 x Cd x Reference Area
Cd From a Wind Tunnel Test
While a Cd of 0.75 is a reasonable value to use in a simple model rocket simulation, you could put your rocket into a wind tunnel and measure the drag force acting on it.
You can assume a “standard day” where the air density is 0.00237 slug/ft3. You will also need to accurately measure the velocity of the airflow in the tunnel. The reference area is the area of the body tube when viewed from the end. Once you have measured the drag you have everything you need to calculate the drag coefficient. This is done using the drag equation:

## Slide 34
We apply some algebra to the drag equation to come up with an equation that allows us to calculate the Cd.
2 x Drag
Cd = ------------------------------------------------------------
Air Density x Velocity2 x Reference Area
Cd From a Wind Tunnel Test
If you are building a big rocket, you can make a smaller model to place in the wind tunnel – as long as it has the same shape and proportions. Calculate the Cd of the model using the reference area of the model. Then, when calculating the drag on the actual rocket, use the full scale rocket’s reference area. This “reference area” allows you to scale the drag…

## Slide 36
Questions ?