## Slide 1
Basic Orbital Mechanics
Practice Problems
LabRat Scientific
2018 ©

## Slide 2
Calculate the orbital velocity of a satellite in a 500 mi. high circular Orbit.
First – convert the altitude to feet:
Orbital Altitude = 500 mi * 5,280 ft/mi = 2,640,000 ft
Next – calculate height above the center of the earth:
Orbital Radius = 2,640,000 ft + 20,900,000 ft = 23,540,000 ft
Finally – calculate the orbital velocity:
U 14.05 x 1015 ft3/sec2
VelocityCircular = ----------------- = ---------------------------------
Orbit Radius 23,540,000 ft
VelocityCircular = 24,431 ft/sec

## Slide 3
Calculate the perigee and apogee velocities for a satellite in an orbit having a perigee of 100 mi and an apogee of 1000 mi.
Calculate the spacecraft velocity and perigee and apogee for an elliptical orbit that has an perigee of 100 miles and an apogee of 1,000 miles.
First, calculate the apogee and perigee in feet –
Perigee (ft) = 100 mi * 5,280 ft/mi = 528,000 ft
Apogee (ft) = 1,000 mi * 5,280 ft/mi = 5,280,000 ft
Next, calculate the apogee and perigee above the center of the earth –
Perigee (ft) = 20,900,000 ft + 528,000 ft = 21,428,000 ft
Apogee (ft) = 20,900,000 ft + 5,280,000 ft = 26,180,000 ft

## Slide 4
Next, calculate the length (2a) of the major axis of the ellipse –
2a = 21,428,000 ft + 26,180,000 ft = 47,608,000 ft
2a
Next, calculate the orbital energy (E) –
U 14.05 x 1015 ft3/sec2
E = - -------- = - ------------------------------- = - -295,118,467 ft2/sec2
2a 47,608,000 ft
Don’t forget that this is a “negative” number…

## Slide 5
U 14.05 x 1015 ft3/sec2
VelPerigee = 2 * ( E + -------------------- ) = 2 * (- 295,118,467 ft2/sec2 + -------------------------- ) Perigee Radius 21,428,000 ft
VelPerigee = 26,854 ft/sec = 18,309 MPH
U 14.05 x 1015 ft3/sec2
VelApogee = 2 * ( E + -------------------- ) = 2 * (- 295,118,467 ft2/sec2 + -------------------------- ) Perigee Radius 26,180,000 ft
VelApogee = 21,980 ft/sec = 14,986 MPH

## Slide 6
Calculate the orbital energy of an elliptical orbit that has a perigee of 700 mi and an apogee of 2,000 mi.
First – convert the altitudes to feet:
Perigee Altitude = 700 mi * 5,280 ft/mi = 3,696,000 ft
Apogee Altitude = 2,000 mi * 5,280 ft/mi = 10,560,000 ft
Next – calculate the heights above the center of the earth:
Perigee Radius = 3,696,000 ft + 20,900,000 ft = 24,596,000 ft
Apogee Radius = 10,560,000 ft + 20,900,000 ft = 31,460,000 ft
Next – calculate the major axis (2a) of the ellipse:
2a = 24,596,000 ft + 31,460,000 ft = 56,056,000 ft
Finally – Calculate the energy (E):
14.05 x 1015 ft3/sec2
E = - ----------------------------- = - 250,642,215 ft2/sec2
56,056,000 ft