## Slide 1
Flight
Parachute Opening Loads
LabRat Scientific
© 2019

## Slide 2
Parachute design is much more complex than just selecting a parachute shape and sizing the canopy. A parachute must be able to withstand potentially heavy loads during deployment.
The designer must select the proper materials, design the stitching techniques to hold things together, and incorporate ways to minimize the opening loads.
It’s not good enough to just build the parachute super strong because this will probably result in a parachute that is too bulky and too heavy.
Generally speaking, the biggest design consideration is the Opening Shock Load because it will drive the required strength of the system…

## Slide 3
The opening shock can be so high that the parachute will tear to shreds or rip away from the payload?

## Slide 4
“Infinite Mass” is a condition where the descending body does not decelerate when the chute is deployed. This is what happens when a chute is deployed in a wind tunnel (the air speed does not decrease…).
Parachute Opening Load
This is the “opening shock” - the time when the parachute is most likely to fail…
Steady State Drag

## Slide 5
What causes the large Opening Load

## Slide 6
What causes the large Opening Load

## Slide 7
As the parachute canopy begins to open it starts scooping up air that “is at rest”. This “resting” air has inertia and thus wants to resist being accelerated…
What causes the large Opening Load

## Slide 8
The moving payload body also has inertia and it wants to resist being decelerated… These opposing inertial states cause the large opening force to exist in the system.
What causes the large Opening Load

## Slide 9
Once the captured bubble of air is accelerated and the system reaches a steady state condition the inertial imbalance becomes greatly diminished and the loads in the system decrease.
What causes the large Opening Load

## Slide 10
Estimating Parachute Opening Loads
Opening Shock = ½ x Air Density x Vel2 x Cd x Area x X0 x X1
X1 = Opening Shock Decrease Factor (dependent on operating conditions)
X0 = Opening Load Shock Factor (dependent on chute shape)
Standard Drag Equation
Factors X0 and X1 are determined experimentally…
The Handbook of Astronautical Engineering (Koelle) provides an equation for estimating parachute opening shock:

## Slide 11
X0 = Opening Load Shock Factor
Flat Circular Parachute: X0 = 1.7
Square Parachute: X0 = 1.7
Cross Parachute: X0 = 1.3
Opening Load Factors
This factor is driven by the shape and porosity of the parachute canopy.
Note: Data on full-scale parachute Opening Shock Factors is very limited

## Slide 12
1.0 > X1 > 0.02
Infinite Mass Conditions
Large Drag and Low Weight Conditions
X1 = Opening Shock Decrease Factor
Opening Load Factors
This factor is driven by the canopy loading, canopy filling time, velocity, and altitude during parachute ejection. The range for X1 for full-scale parachutes is as follows:
Infinite mass is a condition where the system velocity does not change once the parachute is deployed. Examples include wind tunnel tests and drop tests of small parachutes with heavy suspended loads. Small values of X1 are associated with systems that slow down very quickly once the chute is deployed such as in large, lightly loaded parachutes deployed at low velocities or light weight model rockets.

## Slide 13
Parachute Opening Load
Experiments

## Slide 14
The Load Cell is attached to the free falling Test Block. The Load Cell measures the parachute opening force.
The Test Block is dropped from several different heights and allowed to freefall prior to parachute extraction in order to generate various parachute extraction velocities.
The Test Parachute is connected to the load pin on the Load Cell
Test Block
Guide Wires
Test Stand
Load Cell
Test Parachute
Opening Load Test Apparatus

## Slide 15
Test Parachute in the Deployment Tube
Ready for drop test. Slack in string is to allow for predetermined freefall before chute extraction.
Opening Load Test Apparatus

## Slide 16
Parachute Extraction
Parachute Inflation
Parachute Full Open
Parachute Opening Sequence

## Slide 17
Drop Test Data
Parachute Opening
Parachute Extraction from Storage Tube
Free Fall of Test Weight
1.32 N
0.302 sec
0.622 sec
(0.32 sec)
Representative Data Sample (0.5 m freefall drop)
Parachute Fully Open

## Slide 18
Drag decreasing towards steady state drag
Drag as the parachute canopy opens
Test Rig hitting the ground
The system does not have sufficient time (vertical distance) to allow the chute to reach steady state drag level.
Drop Test Data
Parachute Opening Time
(0.154 sec)

## Slide 19
Chart: Opening Load vs. Velocity
| 2.25 | 3.14 | 4.4000000000000004 | 5.19
 | 1.045 | 1.46 | 1.8825 | 2.0833
Drop Test Data

## Slide 20
Extraction Velocity (m/sec) | Opening Load (N) | Steady State Drag (N)
2.25 | 1.05 | 0.27
3.14 | 1.46 | 0.52
4.4 | 1.88 | 1.02
5.19 | 2.08 | 1.42
The Steady State Drag is calculated by using the Extraction Velocity in the drag equation. The Opening Load is the maximum force that was measured during the drop tests. The difference in these load values represents the Opening Shock.
Drop Test Data

## Slide 21
Calculating the Opening Load Shock Factor
The Opening Load Shock Factor (X0) is calculated by dividing the measured opening load by the calculated steady stage drag.
Measured Opening Load
Opening Load Shock Factor (X0) = -----------------------------------------
Calculated Steady State Drag
LabRat drop tests indicate that the Opening Load Shock Factor (X0) is not linear for small model rocket parachutes and thus an equation must be established so that values can be estimated for cases not directly tested.

## Slide 22
Opening Shock = ½ x Air Density x Vel2 x Cd x Area x X0 x X1
Chart: Shock Factor
| 2.25 | 3.14 | 4.4000000000000004 | 5.19
 | 3.8704 | 2.8077 | 1.8456 | 1.4671
Using a function in Excel, a polynomial curve fit was applied to the test data in order to generate an equation for estimating the Opening Shock Factor (X0) for the small flat circular parachute used in the drop tests.
Since the tests were conducted under infinite mass conditions, the Opening Shock Decreasing Factor (X1) is assumed to be 1.0.
Establishing an Equation for X0

## Slide 23
Estimating Opening Loads for Model Rockets
Use the following equation to estimate the Opening Load Shock Factor:
X0 = ( 0.17 x (Rocket Velocity)2 ) - ( 2.09 x (Rocket Velocity) ) + 7.7
Assume one of the following Opening Shock Decreasing Factors:
X1 = 0.08 for a light weight model rocket
X1 = 0.12 for a medium sized high-powered model rocket
X1 = 0.20 for a heavy, high-flying high-powered model rocket

## Slide 24
Sample Calculation
Calculate the opening load for a 50 cm diameter flat circular parachute on a light-weight model rocket flying at 10 m/sec when the parachute is deployed.
1. Calculate the Canopy Area (S):
Area = Pi x Radius2 = 3.1416 x (0.25 m)2 = 0.20 m2
2. Calculate Parachute Drag at Deployment:
Drag = ½ x Density x Velocity2 x Cd x S = 0.5 x 1.225 x (10)2 x 1.3 x 0.2
= 15.9 N
3. Calculate Opening Load Shock Factor (X0):
X0 = ( 0.17 x (Rocket Velocity)2 ) - ( 2.09 x (Rocket Velocity) ) + 7.7
X0 = ( 0.17 x (10)2 ) - ( 2.09 x (10) ) + 7.7
X0 = 3.8

## Slide 25
Sample Calculation
4. Select an appropriate Opening Shock Decrease Factor (X1):
X1 = 0.08 Since we are analyzing a light-weight model rocket
5. Calculate the Opening Shock:
Opening Shock = Drag x X0 x X1
= 15.9 N x 3.8 x 0.08
= 4.8 N
This value is significantly lower than the “drag” calculated in Step 2 because the rocket is light weight and the system slows down extremely fast. While the deceleration will be high, the light weight rocket results in a small load… In contrast, a very heavy rocket with the same chute and deployment conditions would have an opening shock on the order of 12 N.

## Slide 26
Reducing Opening Shocks

## Slide 27
What can be done to minimize the opening loads?
1. Make the parachute open slower
4. Make a shock absorbing system
2. Use a more porous canopy material
3. Use an apex vent

## Slide 28: Canopy Area Control – Staging and Reefing
Reefing is the technique of holding the base of the parachute canopy partially close by a loop of rope. The rope is cut by pyrotechnic line cutter a few seconds after parachute opening.
Staging is the technique of using multiple parachutes and opening them in a controlled sequence.
While reefing is not practical in model rockets, staged recovery systems are routinely used in high-powered hobby rockets.

## Slide 29: Reefed/Disreefed Parachute
Representative load had the chute not been reefed
This graph shows how the loads occur in “steps” as the result of reefing. The maximum deceleration ends up being less than an un-reefed system.

## Slide 30: Permeable Materials
Also known as “porosity”
Allows more air to move through the canopy material and thus reduces the mass of air that needs to be accelerated during parachute opening.
Affects the following
  Drag Coefficient
  Stability (swinging)
  Inflation time
  Opening shock
Caution - If the canopy is too porous it may not open.

## Slide 31: Apex Vent
The apex vent allows air to escape from inside the canopy, resulting in lower internal pressure.
Less internal pressure will alter inflated shape of the canopy and thus the drag area.
If more air is allowed to pass through the apex hole the air mass that needs to be accelerated is decreased.
Caution - If the vent is too large, the internal pressure will be to low and the canopy may not inflate.

## Slide 32
A large rubber band that stretches and dissipates energy…
A heavier elastic cord could be used for bigger rockets. Generally, the longer the better to give more stretch….
Elastic Band
Shock Absorption

## Slide 33
Simple Cord
The cord provides no elasticity and thus no shock attenuation.
Shock Absorption

## Slide 34
Slip Loops
Loops of string tightly tied around the lanyard loops.
Shock Absorption

## Slide 35
The line tension causes the lanyard to pull through the string ties which dissipates energy (load).
Slip Loops
Shock Absorption

## Slide 36
Thread sewn through the lanyard. The thread has to break to release the loops.
Break Loops
Shock Absorption

## Slide 37
As the thread ties “snap” they dissipate energy…
Snap!
Snap!
Break Loops
Shock Absorption

## Slide 38
Shock Attenuation Experiments

## Slide 39: Shock Attenuation Testing
A simple static pull test is not adequate to assess “snatch loads” and “shock attenuation” because shock loading is a short duration “dynamic” element
  It needs to have a “snatch” element rather than just a simple “static” load

## Slide 40: Shock Attenuation Test Apparatus
Load Cell
Shock attenuation device being subjected to test
Test Block
Guide Wires
Test Stand
In this test configuration, the load cell it attached to the top of the Test Stand.
Simple drop tests can be used to assess various shock attenuation techniques.
Trial-and-Error tests on a stiff cord are conducted to determine a free fall drop height that gives a peak load cell reading that is equal to the anticipated opening load.
A freefalling Test Block is used to jerk on the test material.

## Slide 41
Force Sensor
Drop Weight
Test Material
Shock Attenuation Test Apparatus

## Slide 42
Chart: Cotton String
Shock Attenuation Test Results
The example calculation provided on an earlier slide generated an opening load estimate of 4.8 N. The experimental freefall height was determined by trying various drop tests using the stiff cotton string. A 5 cm drop height resulted in a 5.4 N test shock load.
Chart: Elastic Band
An elastic band was tested using the same 5 cm drop height and drop mass. The difference in the shock load represents the shock attenuation.

## Slide 43
Chart: String vs. Elastgic Band
This side-by-side comparison shows how the shock load is significantly reduced by incorporating an elastic band into the parachute train.
Notice that while the load is lower, the action time is quite a bit longer for the elastic band.
Shock Attenuation Test Results

## Slide 44
Additional tests at higher opening loads were conducted to compare the performance of the following techniques:
      Stiff Cord
      Break Loops
      Large Elastic Band

## Slide 45
Chart: Rigid Cord
Initial Snatch
First Bounce
Second Bounce
This configuration provides no shock attenuation.
This is a test of a cotton cord that had very little elasticity and thus very little shock attenuation. It represents the worst-case scenario.
400 samples/sec

## Slide 46
Chart: Slip Loops (4 ea) – Kite String Restraint Loops
400 samples/sec
This drop test utilized the tied restraint loops. It resulted in multiple load pulses as each loop pulled tight.
The maximum load was 12 N compared to 40 N using the simple cord.

## Slide 47
Chart: Elastic Band
400 samples/sec
This drop test utilized an elastic band which is typical for a simple model rocket.

## Slide 48
Chart: Attenuation Comparison (3 techniques)
 | -0.027168 | -0.027168 | 0.0062695 | 0.0062695 | 0.0062695 | 0.0062695 | 0.0062695 | 0.0062695 | 0.073145 | 0.073145 | 0.2048 | 0.30512 | 0.60397 | 0.93834 | 1.3375 | 1.9686 | 3.1013 | 4.5997 | 6.629 | 9.5569 | 14.1838 | 19.7093 | 25.4 | 29.7928 | 34.5869 | 39.0467 | 40.5095 | 39.845 | 38.5806 | 35.2181 | 29.728 | 23.5024 | 18.3447 | 14.2506 | 10.6896 | 7.3939 | 4.7648 | 3.0679 | 1.9038 | 1.1369 | 0.67084
0.8 Sec
0.3 Sec
0.06 Sec
400 samples/sec
The elastic band stretched out the reaction time and resulted in the lowest snatch force acting on the system.
Rigid Cord

## Slide 49
Experiment Suggestions
Effect of Apex Vent size on opening loads
  Build several canopies with identical area and cut various size holes at the apex.
Effect of canopy porosity on opening loads
  Build several canopies with identical areas and use a paper punch to perforate the canopies with different number of holes. Calculate the total area of the holes in each canopy and calculate a porosity ratios (Rp = Total Hole Area / Canopy Area)
Effect of elastic band length of shock attenuation

## Slide 50
Questions?