## Slide 1: Robotics Belts, Chains, Sprockets and Gears
LabRat Scientific
© 2018

## Slide 2
When designing a robot, it will be necessary to transfer the motion and power generated by a motor to devices such as wheels, spinning devices, or arms. There are several ways to accomplish this: Belts and Pulleys, Chains and Sprockets, or Gear Systems.
These systems can also be used to increase or decrease rotational speed and change the torque of the system.

## Slide 3: Components
Conveyor Belt
Drive Belt (toothed)
Drive Chain
Sprockets

## Slide 4: Applications
Transmit power or rotation over a distance…
Alter torque and rotational speeds
Move an object back and forth in a linear fashion…

## Slide 5: Picking up a Ball
A pair of belts can be used to puck up a ball. When the belts rotate in one direction, they will draw the ball in. When the belts are reversed, they will push the ball out.
Wide, flat belts can be used or a series of parallel narrow bands (surgical tubing) can be used. Both have been used successfully.

## Slide 6: Surgical Tubing
The system depicted here is used ot move balls within the robot. The distance between pulleys can’t be too far because the tubing will spread apart and not grip the ball properly.

## Slide 7: Surgical Tubing Coupler
Surgical tubing is hollow. A small wood or plastic dowel can be inserted in the open ends of the tube to serve as a coupler.
If the fit is tight enough, the dowels can secure the tube by themselves. It may be necessary to use tape or wire rings to keep the tube from slipping off.

## Slide 8
Pulleys and Sprockets are essentially the same thing. Pulleys are used in conjunction with belts, and sprockets are used in conjunction with chains.
Chains and sprockets provide much more positive engagement and the system will not slip. Belts and pulleys much be tight to the belt doesn’t slip.
Gears work in the same way, but there is no need for belts or chains to connect them. Gears interact directly with one another.

## Slide 9
Changing the diameters of the sprockets or pulleys will result in changes in rotational speed and delivered torque. This is discussed in the following slides.

## Slide 10: Sprocket Ratios
5
10
15
20
25
30
34
5
10
15
16
16
Ratio = -------- = 0.47
34
34
Ratio = -------- = 2.125
16

## Slide 11: Nomenclature
PRIMARY SPROCKET
The sprocket that is attached to the power generating device (i.e. motor). It creates the tension (force) in the chain.
SECONDARY SPROCKET
The sprocket that is driven by force in the chain created by the primary sprocket

## Slide 12: Sample Problem
Primary Sprocket: 30 teeth
Secondary Sprocket: 15 teeth
If the motor turning the primary sprocket is turning at 100 rev/min, how fast will the secondary sprocket be spinning?
Primary
30 teeth
Sprocket Ratio = ---------------- = 2
15 teeth
Secondary Rotational Speed = Primary Rotational speed x Sprocket Ratio
200 rev/min = 100 rev/min x 2

## Slide 13: Effect of Sprocket Ratio
PRIMARY SPROCKET
PRIMARY SROCKET
Speed: Increases
Torque: Decreases
Speed: Decreases
Torque: Increases
Effect on Free Sprocket
SECONDARY SROCKET
SECONDARY SROCKET

## Slide 14
Primary Sprocket
Puts heavier initial mechanical load on the motor
  Initial motor current draw will be high
Results in low acceleration
  Not good for zipping back and forth
Provides high top-end speed
  Good if you need high speed over long distance
Not good for hill/ramp climbing
Effect of Sprocket Ratio

## Slide 15
Results in low initial mechanical load on the motor
  Current load minimized
Can provide best acceleration if sprocket ratio is optimized
  Good if lots of starting and stopping is required
Results in low top-end speed
Good for hill/ramp climbing
Primary Sprocket
Effect of Sprocket Ratio