## Slide 1: Robotics Generating Torque
LabRat Scientific
© 2018
Force
Distance
The torque is about Point A
A
Rotation
45

## Slide 2
TORQUE
A rotational “force”
Units example = Foot Pounds
Equation:
Torque = Force x Distance
Force
Distance
The torque is about Point A
A

## Slide 3
The “proper” force must be used in the equation.
The force used must be the force that is acting “tangential” to the rotation of the object.
Is the GREEN Arrow the “tangential” component?
No - In this case, the RED Arrow represents the component of the force acting tangential to the rotation of the beam.
For this example, lets assume the force (BLUE Arrow) is pointing at an angle that is 45 degrees off of vertical.
Force
Distance
The torque is about Point A
A
Rotation
45

## Slide 4: This becomes a Trigonometry Problem
45
Trigonometry is the “math” of dealing with triangles. A very important concept in engineering.
We need to know the “internal” angles of the triangle… Is it possible to determine the internal angles of this triangle?
First, we are working with force components, so engineers want to work with “right triangles”. This means that one angle is going to be 90 degrees.
90
Because engineers like to work in an “orthogonal” manner, This angle is also 90 degrees…
So we can calculate this internal angle to be 45 deg (90 – 45 = 45)…
45
45
Trigonometry says the sum of the internal angles of a triangle is 180 degrees. Thus, the final missing angle is 45 deg (180 – 90 – 45 = 45).

## Slide 5
90
45
45
50 lbs (given)
Sine (angle) = Opp / Hyp
Opp = Hyp x Sine (angle)
Cosine (angle) = Adj / Hyp
Adj = Hyp x Cosine (angle)
Opp = 50 lbs x Sine (45)
= 35.4 lbs
Adj = 50 lbs x Cosine (45)
= 35.4 lbs
Lets assume the force acting on the beam is 50 pounds…

## Slide 6
Force
Distance
The torque is about Point A
A
Rotation
35.4 lbs
If the distance between the force and the beam’s pivot point is 2 feet, then the resulting torque is calculated as follows:
Torque = Force x Distance
= 35.4 lbs x 2 ft
= 70.8 ft lbs
If we attached a motor at Point A, it would have to have a torque of 70.8 ft-pounds to keep the beam from rotating…
Here is what our system looks like…
2 ft

## Slide 7
In a robot, torque is usually generated by a motor of some sort.
Motors will rarely have the exact torque or speed you need to accomplish some function…
Luckily gears, belts, chains, pulleys, and sprockets can be used to alter torque and speed.

## Slide 8
Let’s look at how we can use two different size sprockets and a chain to change the rotational speed of the system. In this example a motor is attached to a small sprocket and a chain is then connected to a bigger one. The relevant data is provided below.
12 sprockets
Sprocket Dia = 1.5” = D
Circumf = Pi * D = 4.7”
26 sprockets
Sprocket Dia = 3.2” = D
Circumference = Pi * D = 10.1”
12 sprockets 4.7”
Ratio = ------------------ or ----------- = 0.46
26 sprockets 10.1”
Motor
88 Rev/Sec
The first thing we need to know is the sprocket ratio. It is calculated as follows:

## Slide 9
88 rev/sec
x 0.46
Rotational
Speed of big =
Sprocket
= 40.5 rev/sec
Sprocket Ratio
Rotational Speed of the motor
88 rev/sec
40.5 rev/sec
The sprocket ratio can then be used to determine how fast the big sprocket will spin.
The sprocket system cuts the rotational speed in half (a little bit more than half to be precise…

## Slide 10
GIVEN: Motor Torque = 10 in-lb
Electric Motor
Chains and sprockets can be used to change Torque

## Slide 11
Motor Torque = 10 in-lb
Force = Motor Torque / Sprocket Radius
Force = 10 in-lb / 5 in
Torque = Force x Distance
Force = 2 lb
Radius = 5 in.
2 lb
For a pulley, sprocket, or gear the “distance” is the radius of the pulley, sprocket, or gear. As such, the torque equation becomes the following: Torque = Force x Radius
The torque being generated by the motor converts to a force at the edge of the sprocket. The resulting force is calculated as follows:

## Slide 12
Force = 2 lb
The force acting a the edge of the small sprocket is transmitted to the chain. As such the chain is under a “tension”.

## Slide 13
Force = 2 lb
The tension in the chain then applies a force to the edge of the larger sprocket.

## Slide 14
Force = 2 lb
Radius = 10 in.
Torque = Force x Radius
Torque = 2 lb x 10 in
Torque = 20 in-lb
The motor produced 10 in-lb of torque, but now the big sprocket is producing 20 in-lb of torque. This comes at a cost – the rotational speed of the big sprocket decreases…
The force then creates a torque about the axle of the larger sprocket.
The torque is calculated as follows:

## Slide 15
Circumference A = Pi x Dia = 3.1416 x 10 in = 31.4 in
Circumference B = Pi x Dia = 3.1416 x 20 in = 62.8 in
The small wheel must rotate twice to get the big wheel to spin once
A
B
5 in
10 in
Circumference is a function of Diameter…
As the system torque increases, the rotational speed of he system decreases.

## Slide 16
What happens to the rotational speed?
The big wheel spins half as fast as the smaller wheel…

## Slide 17
Power = Torque x Rotational Speed
In our example, if the TORQUE is doubled and the ROTATIONAL SPEED is halved, what happens to the POWER?
The POWER remains constant…

## Slide 18: Summary
Sprocket A -> Sprocket B | Rotational Speed Change | Torque Change
SMALL to BIG | Slows Down | Goes Up
BIG to SMALL | Speeds Up | Goes Down
Belts must be tight. If they are not tight they can slip
Chains do not slip because they use sprockets with teeth
A few things to remember:
Belt slip can be eliminated by using toothed belts

## Slide 19
Gears works just like chains and sprockets, except the gears have to be touching one another…
GEARS

## Slide 20
GEARS
The same theories concerning torque and speed are at play when gears are used…

## Slide 21
Sample Problem
Motor
We know from earlier in the lesson, we need to go from a small gear to a large gear to reduce the rotational speed.
First, lets calculate the speed ratio:
Desired Speed 200 RPM
Ratio = --------------------- = ------------- = 0.1
Motor Speed 2000 RPM
Next, lets go to the parts box and find a small gear. We will pretend we found a 0.5” radius gear….
Now, using the basic information we have, we can calculate the required size of the second gear…
You have a motor which spins at 2000 rev/min, which is way too fast for your application! You need to cut down the speed to 200 rev/min. What are you going to do?

## Slide 22
Sample Problem
Motor
Speed Ratio = Gear Ratio = Radius Ratio
Small Gear Radius 0.5 in
Radius Ratio = ------------------------- = ---------------------
Big Gear Radius Big Gear Radius
0.5 in
0.1 = -------------------------
Big Gear Radius
0.5 in
Big Gear Radius = --------------- = 5.0 in
0.1
The “circumference” is the important geometric element when sizing gears, BUT since Circumference = (2 x Radius) x Pi everything is in a 1-to-1 ratio. Because of this we can make our calculations based on either radius, diameter, or circumference… Lets use radius, since we have defined the first gear as a 0.5” radius.

## Slide 23
YIKES! That’s a huge gear…

## Slide 24
This gearing arrangement can solve the BIG gear issue…
Rad = 0.5 in
Rad = 2 in
Rad = 0.5 in
Rad = 1.25 in
Blue Gear to Big Red Gear:
0.5 in
Ratio = ---------- = 0.25
2.0 in
Big Red Gear Speed = 0.25 x 2000
= 500 RPM
Blue Gear spinning at 2000 RPM
Little Red Gear is spinning at same speed as Big Red Gear since they are fused together…
Small Red Gear Speed = 500 RPM
Small Red Gear to Orange Gear:
0.5 in
Ratio = ---------- = 0.4
1.25 in
Orange Gear Speed = 0.4 x 500
= 200 RPM