## Slide 1
Rockets
The Rocket Equations
LabRat Scientific
© 2018

## Slide 2
Delta-Velocity ( ∆V)
In order to reach orbit the rocket must achieve a specific velocity. The rocket must be launched from the surface of the earth and fly an elliptical trajectory to the height of the desired circular orbit - this is the initial Delta-V maneuver.
The rocket must then perform a second Delta-V maneuver to circularize the orbit. This means that at least two Delta-V maneuvers are required.
The equation on the next slide determines this total theoretical Delta-V
Delta-V1
Delta-V2

## Slide 3
re = Radius of Earth = 20,900,000 ft
r2 = Radius of Orbit = re + Orbit Height above Surface (ft)
μ = Gravity Constant = 1.41 x 1016 ft3/sec2
Calculating Launch Velocity to get to a Circular Orbit
2 1
Vlaunch = μ ( --------- - ---------- )
re r2

## Slide 4
Chart: Launch Delta-V to get to target circular orbit (non-spinning Earth)
| 100 | 200 | 300 | 400 | 500 | 600
 | 26292 | 26631 | 26948 | 27246 | 27524 | 27788
The Launch Velocity equation was used to generate this plot for multiple target orbits.

## Slide 5
Delta-Velocity ( ∆V)
The Launch Velocity equation used in the previous charts is theoretical and assumes a non-spinning earth.
The rotation of the earth creates a tangential velocity at the earth’s surface and this velocity can assist the rocket if it is launched towards the east. This effect will reduce the amount of Delta-V required.
However, there are also Delta-V “losses” due to the rocket weight and aerodynamic drag which must be accounted for. These losses increase the Delta-V requirement and must be included in the calculations.

## Slide 6
Ꙍearth = 0.000073 rad/sec
(rotational rate of Earth)
rearth = 20,900,000 ft (at the equator)
The further north the launch site, the smaller the earth’s radius at that location.
Earth’s Rotational Velocity and its Contribution to Launch Delta-V
If the rocket is launched eastward from the equator, the rotation of the earth will provide the following initial velocity:
Velsurface = Ꙍearth * Radius
= 0.000073 rad/sec * 20,900,000 ft
= 1,526 ft/sec
Radius (r)

## Slide 7
The closer the rocket is to the equator, the larger the radius of the earth. This larger radius results in a higher tangential velocity. This is why most launch sites are located at lower latitudes and are situated where the rockets can be launched towards the east (Cape Canaveral in Florida for example).
Eastward Launch Directions

## Slide 8
Delta-V Losses
The rocket equations do not account for two critical factors – offsetting the weight of the rocket (gravity effect) and drag. Drag is obviously the affect of the air resistance acting on the rocket. The gravity effect involves the “weight” of the rocket. A portion of the thrust simply goes to supporting the weight of the rocket, and that portion of thrust does not provide any effective Delta-V. For example, a rocket motor producing 10,000 lbs. of thrust on a 10,000 lb. rocket will result in an acceleration of zero . This means that 10,000 lbs. of thrust is not contributing to the Delta-V of the rocket.
As such, we must account for these factors in the target Delta-V we are going to design to. These factors are known as “velocity losses”. Decades of rocket design have shown that typical losses are as follows:
Gravity losses = 6,000 to 8,000 ft/sec.
Drag losses = 1,500 to 2,000 ft/sec.

## Slide 9
Large component of gravity “fighting” the thrust – thus high gravity losses
Gravity Losses
Smaller component of gravity “fighting” the thrust – thus low gravity losses
The ascent trajectory can be optimized (i.e. made flatter) in order to minimize the gravity losses.

## Slide 10
Thrust
Drag
Drag Losses

## Slide 11
Satellite
Vehicle Electronics (telemetry, flight termination receiver, separation system, etc)
What is sent into Orbit ?
For this demonstration, the weight of the satellite and the vehicle electronics is defined as 400 lbs.
While this is actually the “payload” for the entire rocket, in this computational method it is referred to as the “payload for the 2nd stage”. This will make a little more sense in the following two slides…

## Slide 12
“Payload” for 2nd Stage
The 2nd Stage “Stage Weight” includes these major elements.

## Slide 13
“Payload” for 2nd Stage
The 2nd Stage “Stage Weight” includes these major elements.
The first set of calculations will estimate the combined weight of the payload (satellite and vehicle electronics) and the 2nd stage motor, fuel tank, fuel, and structures.

## Slide 14
“Payload” for 1st Stage
The 1st Stage “Stage Weight” includes these major elements.
This also represents the total weight of the complete vehicle and satellite.
The second set of calculations will estimate the combined weight of the payload (satellite and vehicle electronics); 2nd stage motor, fuel tank fuel, and structures; and 1st stage motor, fuel tank, fuel, and structures.

## Slide 15
The following equations are known a the “Rocket Equations” and are used to estimate the weight of a rocket’s fuel and structure in order to achieve a specific orbital altitude.

## Slide 16
Effective Exhaust Velocity (c)
The overall size of an orbital launch vehicle is dictated in part by the “impetus” of the rocket motor(s). The “impetus” is defined by how fast the exhaust gasses are exiting the rocket motor. This is known as the Effective Exhaust Velocity (c) and it is calculated as follows:
c = Gravity Accel * Engine Specific Impulse
c = g * ISP
“g” is the acceleration due to gravity and the ISP is the specific impulse of the rocket motor(s) - see next slide.

## Slide 17
Specific Impulse (ISP)
Rocket Motor Type | Specific Impulse (ISP)
Solid | 230 – 280 (sec)
Liquid | 300 – 420 (sec)
Hybrid | 280 – 350 (sec)
This parameter defines the “energy rating” of the rocket motor. The Total Impulse is the area under the Thrust vs. Time curve. Specific Impulse is the Total Impulse divided by the fuel weight that the motor burns. The higher the ISP the more energetic the rocket motor…
From this table you can see that liquid rocket motors tend to be the most powerful.

## Slide 18
∆V
MR = ln-1 --------
c
= e (∆V/c)
MR = 2.718 (∆V/c)
Stage Mass Ratio (MR)
The term ln-1 is the “inverse natural log”. It is left to the student to refresh their memory on how this term becomes 2.718 (∆V/c)
This term represents the ratio of the total initial mass (weight) of the rocket stage to the final mass (weight) of the rocket stage after the fuel is expended. So, MR = ( MassFueled / MassEmpty ). The actual masses are not known, but the following equation can be used to determine the ratio:

## Slide 19
Fuel Mass Fraction (MF)
The weight of the fuel needed for a particular stage is estimated as a function of the Stage Mass Ratio (MR). The MF is the ratio of the fuel weight and the total stage weight (thus, MF = Fuel Weight / Stage Weight ). Since we don’t know these weights at this point we can calculate the MF using the following equation:
1
MF = 1 - -----------
MR
The actual weight of the fuel is calculated by multiplying the MF by the total weight of the stage. These parameters are calculated in the following slides…
This number could approach 1.0, but that it not really viable. A value of “1.0” would indicate that the stage is 100% fuel with no structure. A value of 0.8 or more means the structure is very efficient.

## Slide 20
Note:
The Stage Mass Ratio (MR) and the Fuel Mass Fraction (MF) use the terminology “mass”. In actuality, these terms are unitless ratios and thus “weight” can be interchanged with “mass”.
In the equations on the following slides, if we want to know the rocket parameters in “pounds” we use weight units (lbs) for the payload. If we want to know the rocket parameters in “kilograms” we use mass units (kg) for the payload.

## Slide 21
Stage Weight
The estimated weight of a given stage is a function of the payload weight, the assumed Structural Ratio (SR), and the Fuel Mass Fraction.
Payload Weight
-------------------------------
Stage Weight = MF
1 - ------------
( 1 – SR )

## Slide 22
Fuel Weight
Fuel Weight = MF * Stage Weight
The weight of the fuel in each stage is calculated using the following equation:

## Slide 23
Structural Weight
Stage Type | Structural Ratio (SR)
Booster | 0.08 - 0.2
Upper | 0.07 – 0.15
The structural weight is the weight of all the hardware in the rocket stage including fuel tanks, skin, frame work, etc. (essentially everything except the payload and the fuel). It is based on an assumed Structural Ratio (which is selected based on experience) and the weight of the fuel in that stage. More fuel = more structure…
( SR * Fuel Weight )
Stage Structural Weight = -----------------------------
( 1 - SR )
Typical Structural Ratios (SR) are provide in the table below. Booster stages tend to required more and heavier hardware to support the acceleration loads.

## Slide 24
Design Process
Identify the payload weight (this is what is delivered to orbit)
Determine the total Delta-V that is needed based on the desired orbit
Select the number of rocket stages
Identify how much Delta-V will be generated by each stage
Begin calculating various parameters, ratios, and weight values
  c, MR, MF, Stage Weight, Fuel Weight, Structural Weight
  Begin with the upper stage first
Once parameters are calculated for the upper stage, use that total stage weight as the “payload” weight for the stage below. Repeat the process for each stage
Note: Negative calculated values indicate a configuration that is not viable…

## Slide 25
Sample Design Problem
Let’s see if we can estimate the design weight of the SpaceX Falcon 1. This rocket was designed to carry a 400 lb payload to low earth orbit. The published ISP for the 1st stage is 255 sec and the ISP for the 2nd stage is 327 sec.
Let’s assume we want to get to a 100 nmi high circular orbit. Note: a nautical mile (nmi) is 6,080 ft.
ISP = 255 sec
ISP = 327 sec
Nose fairings are usually shed during 2nd stage burn to reduce the 2nd stage weight and improve acceleration. To avoid confusion in this simple analysis we will just ignore the weight of the fairing all together…

## Slide 26
Required Delta-V
Chart: Launch Delta-V to get to target circular orbit (non-spinning Earth)
| 100 | 200 | 300 | 400 | 500 | 600
 | 26292 | 26631 | 26948 | 27246 | 27524 | 27788
Required Delta-V = 26,300 ft/sec - 1,200 ft/sec + 8,000 ft/sec + 1,900 ft/sec = 35,000 ft/sec
The Launch Delta-V to get to a 100 nmi circular orbit is 26,300 ft/sec.
Let’s assume the rotation of the earth provides 1,200 ft/sec of initial velocity.
Let’s assume the gravity losses are 8,000 ft/sec. and the drag losses are 1,900 ft/sec.

## Slide 27
Next, we need to select the Delta-V’s that will be provided by each rocket stage. Let’s assume the 2nd stage provides more Delta-V than the first stage booster:
1st stage ∆V1 = 14,000 ft/sec
2nd state ∆V2 = 21,000 ft/sec.

## Slide 28
Given:
Payload Weight = 400 lbs
Rocket Motor ISP = 327 sec
Assumed:
Structural Ratio = 0.09
Delta-V Contribution = 21,000 ft/sec
We start with the Second Stage
Payload
The actual structural weight ratio is unknown for the Falcon 1, but SpaceX used new light weight materials and construction techniques so we will assume a ratio of 0.09 for each stage.

## Slide 29
The first step is to calculate the Effective Exhaust Velocity (c) of the 2nd stage:
c1 = g * ISP
= 32.2 ft/sec2 * 327 sec
c1 = 10,529 ft/sec

## Slide 30
The next step is to calculate the Stage Mass Ratio (MR):
MR = 2.718 (∆V/c)
= 2.718 ( 21,000 / 10,529 )
MR = 7.35

## Slide 31
The next step is to calculate the Fuel Mass Fraction:
1
MF = 1 - ---------
MR
1
= 1 - ---------
7.35
MR = 0.86
This relatively high number (1.0 is the maximum) indicates that the weight of the 2nd stage is mostly fuel.

## Slide 32
Payload Weight
-------------------------------
Stage Weight = MF
1 - ------------
( 1 – SR )
Now we can calculate the total stage weight for the 2nd stage using the following equation:
200 lbs
-------------------------------
Stage Weight = 0.86
1 - ---------------
( 1 – 0.09 )
Stage Weight = 7,892 lbs

## Slide 33
Now we can calculate the weight of the fuel needed in the 2nd stage:
Fuel Weight = MF * Stage Weight
= 0.86 * 7,892 lbs
Fuel Weight = 6,818 lbs

## Slide 34
Finally, we can calculate the weight of the mechanical structures in the 2nd stage (fuel tank, frame work, etc):
( SR * Fuel Weight )
Stage Structural Weight = -----------------------------
( 1 - SR )
( 0.09 * 6,818 lbs )
= ----------------------------
( 1 - 0.09 )
Stage Structural Weight = 674 lbs

## Slide 35
As a double check, we can add the payload weight, fuel weight and the structural weight together to see how much the 2nd stage weighs:
Stage Weight = Payload Wt + Fuel Weight + Structural Weight
= 400 lbs + 6,818 lbs + 674 lbs
= 7,892 lbs
And this number matches the stage weight calculated in a previous slide…
This weight represents the “payload weight” for the 1st stage calculations

## Slide 36
Payload
Given:
Payload Weight = 7,892 lbs
Rocket Motor ISP = 255 sec
Assumed:
Structural Ratio = 0.09
Delta-V Contribution = 14,000 ft/sec
First Stage

## Slide 37
Once again, the first step is to calculate the effective exhaust velocity of the 1nd stage:
c2 = g * ISP
= 32.2 ft/sec2 * 255 sec
c2 = 8,211 ft/sec

## Slide 38
We will skip the details and show only the computational results for the first stage configuration:
c2 = 8,211 ft/sec
MR = 5.5
MF = 0.82
Stage Weight = 78,235 lbs
Fuel Weight = 64,012 lbs
Structural Weight = 6,331 lbs

## Slide 39
Checking the overall weight of the 2-stage Rocket:
400 lbs Payload weight (the satellite and vehicle electronics)
6,818 lbs 2nd Stage Fuel
674 lbs 2nd Stage Structure
64,012 lbs 1st Stage Fuel
6,331 lbs 1st Stage Structure
------------------
78,235 lbs
The SpaceX Falcon 1 had a total weight of about 61,000 lbs. This estimated value is high, but its in the ball park. In fact, if the 2nd Stage SR is changed to 0.08 and the stage Delta-V’s are adjusted, the total weight gets event closer to 61,000 lbs…
This indicates this method does a reasonable job at estimating rocket weight (size) – as long as reasonable assumptions are made…

## Slide 40
Stage-3 Payload
Stage-2 Payload
Stage-1 Payload
Stage-3 Calculations
Stage-2 Calculations
Stage-1 Calculations
Stage Wt
Stage Wt
Stage Wt = Total Rocket Wt
This method can be expanded to accommodate more stages if desired. The process is exactly the same - the “payload weight” used in the calculations for each lower stage is the weight of the stage sitting on top of it.

## Slide 41
A simple spreadsheet can be built to make these calculations for you. You can then adjust numbers to see if you can create the most efficient (lightest) rocket.
If you get negative numbers during the calculations it is an indication that the combination of inputs you used were not viable.

## Slide 42
Questions ?