## Slide 1
Aerodynamic Stability of Finned Rockets
LabRat Scientific
© 2018

## Slide 2: Basic Concepts
Center of Gravity (CG)
  Point where the mass loads can be concentrated
  Physical balancing point
Center of Pressure (CP)
  Point where aerodynamic forces can be concentrated
  Sort of the aerodynamic balancing point
Static Margin
  Distance between the CG and CP

## Slide 3
Desired direction we want the rocket to fly…
Direction of the airflow…
How does a finless cylinder act in an air flow?

## Slide 4
Desired direction we want the rocket to fly…
Direction of the airflow…

## Slide 5
Desired direction we want the rocket to fly…
Direction of the airflow…

## Slide 6
Desired direction we want the rocket to fly…
Direction of the airflow…

## Slide 7
Desired direction we want the rocket to fly…
Direction of the airflow…
It will tend to orient sideways.
Rockets don’t fly sideways too well…

## Slide 8
Desired direction we want the rocket to fly…
Direction of the airflow…
What can be done to rectify the problem?

## Slide 9
Desired direction we want the rocket to fly…
Direction of the airflow…
Adding fins (not “wings”) will help the situation.

## Slide 10
Desired direction we want the rocket to fly…
Direction of the airflow…

## Slide 11
Desired direction we want the rocket to fly…
Direction of the airflow…

## Slide 12
Desired direction we want the rocket to fly…
Direction of the airflow…

## Slide 13
Desired direction we want the rocket to fly…
Direction of the airflow…
Fins make the rocket “point into the wind”

## Slide 14
Fins are very similar to a wing, but they are designed to work equally well with a positive or negative angle of attack.
Airflow

## Slide 15
Airflow
Fins are very similar to a wing, but they are designed to work equally well with a positive or negative angle of attack.

## Slide 16
Airflow
Fins are very similar to a wing, but they are designed to work equally well with a positive or negative angle of attack.

## Slide 17
Lift
Airflow
Fins are very similar to a wing, but they are designed to work equally well with a positive or negative angle of attack.

## Slide 18
Fins are very similar to a wing, but they are designed to work equally well with a positive or negative angle of attack.

## Slide 19
Fins are very similar to a wing, but they are designed to work equally well with a positive or negative angle of attack.

## Slide 20
Fins are very similar to a wing, but they are designed to work equally well with a positive or negative angle of attack.

## Slide 21
Lift
Fins are very similar to a wing, but they are designed to work equally well with a positive or negative angle of attack.

## Slide 22
Fins are very similar to a wing, but they are designed to work equally well with a positive or negative angle of attack.

## Slide 23
Desired direction we want the rocket to fly…
Direction of the airflow…
The fin lifting force causes the aerodynamic “balancing” point to move back
CP
Without fins…

## Slide 24
Desired direction we want the rocket to fly…
Direction of the airflow…
CP
With fins…
The fin lifting force causes the aerodynamic “balancing” point to move back

## Slide 25
Desired direction we want the rocket to fly…
Direction of the airflow…
Nose cones are added to a rocket to reduce drag, but they can also generate lift which moves the CP forward…

## Slide 26
Desired direction we want the rocket to fly…
Direction of the airflow…
CP
Without Nose Cone…

## Slide 27
Desired direction we want the rocket to fly…
Direction of the airflow…
With Nose Cone…
CP

## Slide 28
Desired direction we want the rocket to fly…
Direction of the airflow…
What happens if we change the size of the fins?
CP

## Slide 29
Desired direction we want the rocket to fly…
Direction of the airflow…
CP
What happens if we change the size of the fins?

## Slide 30
Desired direction we want the rocket to fly…
Direction of the airflow…
CP
Smaller fins = lower stability
What happens if we change the size of the fins?

## Slide 31
Desired direction we want the rocket to fly…
Direction of the airflow…
CP
CG
Static Margin

## Slide 32
Desired direction we want the rocket to fly…
Direction of the airflow…
CP
CG
Static Margin
Smaller Static Margin = lower stability

## Slide 33
Desired direction we want the rocket to fly…
Direction of the airflow…
CP
CG
What happens if we add weight to the nose of the rocket?

## Slide 34
Desired direction we want the rocket to fly…
Direction of the airflow…
CP
CG
What happens if we add weight to the nose of the rocket?

## Slide 35
Desired direction we want the rocket to fly…
Direction of the airflow…
CP
CG
What happens if we add weight to the nose of the rocket?

## Slide 36
Desired direction we want the rocket to fly…
Direction of the airflow…
CP
CG
What happens if we add weight to the nose of the rocket?

## Slide 37
Desired direction we want the rocket to fly…
Direction of the airflow…
CP
Adding weight to the front of the rocket increases stability
CG
Static Margin
What happens if we add weight to the nose of the rocket?

## Slide 38
Desired direction we want the rocket to fly…
Direction of the airflow…
CP
CG
What happens if we add fins towards the front of the rocket?

## Slide 39
Desired direction we want the rocket to fly…
Direction of the airflow…
CP
The CP moves forward due to the fin lift…
CG
What happens if we add fins towards the front of the rocket?

## Slide 40
Desired direction we want the rocket to fly…
Direction of the airflow…
CP
And the stability decreases…
CG
What happens if we add fins towards the front of the rocket?

## Slide 41
Wind
Wind Sensitivity
Moderate Stability
High Stability
A rocket with higher stability will tend to “weather-cock” more than a rocket with less stability.

## Slide 42
Is it possible for a finless rocket to be stable?
What do we need to think about to answer this question?
1. Center of Pressure (CP)
2. Center of Gravity (CG)
What is the key relationship between CP and CG?
CP
CG

## Slide 43: Finless Rocket Experiment
The rocket flew “stable” for a couple of seconds
  It takes time of overcome the inertia
  The rocket must gain speed to build up adverse nose lift
Once it started to diverge, it deviated from stable flight very quickly
Unstable flight during coasting isn’t quite so drastic because the rocket isn’t being pushed
  The rocket tends to tumble rather than fly here and there…
  Drag is high due to high angle of attack
  Trajectory tends to “smooth out“ due to the lack of a thrusting force

## Slide 44
Calculating the Theoretical Location of the
Center of Gravity
and
Center of Pressure

## Slide 45: Center of Gravity
The physical balancing point of the gravity forces
Body Position

## Slide 46: Calculating Center of Gravity
1 lb
2 lb
3 lb
0.5 lb
4 in
20 in
30 in
33 in
CG (in) x total weight (lb) = (4 in)x(1 lb) + (20 in)x(2 lb) + (30 in)x(3 lb) + (33 in)x(0.5 lb)
CG (in) x 6.5 lb = 4 in*lb + 40 in*lb + 90 in*lb + 16.5 in*lb
CG (in) x 6.5 lb = 150.5 in*lb
CG (in) = 150.5 in*lb / 6.5 lb = 23.2 in (measured from Point A)
Sum the moments of the components about Point A, and set equal to the total moment:
A

## Slide 47: Center of Lift (a.k.a Center of Pressure)
The “balancing” point of the lifting forces
Body Position

## Slide 48
4 in
20 in
30 in
33 in
Sum the lift moments of the components about Point A, and set equal to the total moment:
CP (in) x total weight (lb) = (4 in)x(.4 lb) + (20 in)x(.2 lb) + (30 in)x(3 lb) + (33 in)x(1.0 lb)
CP (in) x 1.6 lb = 1.6 in*lb + 4 in*lb + 33 in*lb
CP (in) x 1.6 lb = 38.6 in*lb
CP (in) = 38.6 in*lb / 1.6 lb = 24.1 in (measured from Point A)
0.4 lb
0.2 lb
1.0 lb
Center of Lift (a.k.a Center of Pressure)

## Slide 49
Calculating the lift for the various rocket sections can be a little bit laborious.
In reality, we simplify things by just calculating the Normal Force Coefficients (CN) and skip actually calculating the lift.
Note that the Normal Force Coefficient is the same thing as the Lift Coefficient.

## Slide 50
This approach assumes the straight body tube segmentss do not generate lift. This is a reasonable assumption since the angle of attack of a rocket is generally small.
Parameters used in Calculating Model Rocket Aerodynamics

## Slide 51
Nose Normal Force Coefficient and CP Position
(CN)N = 2.0 this value is a constant regardless of shape and size
0.666 LN
0.466 LN
LN = Nose Length
Ogive
Conical
XN = 0.666 LN
XN = 0.466 LN
Normal Force Coefficient of Nose = (CN)N

## Slide 52
Transition Section Normal Force Coefficient and CP Position
Normal Force Coefficient of the Body Tube = (CN)T
dR 2 dF 2
(CN)T = 2 x -------- - --------
d d
Note: If your rocket does not have a transition section, then this parameter is not calculated…

## Slide 53
LT
XT = XP + -------- 1 + -------------------------------------
3
dF
1 - ---------
dR
dF 2
1 - ------------
dR
Location of Normal Force Coefficient of the Transition = XT
Transition Section Normal Force Coefficient and CP Position
Note: If your rocket does not have a transition section, then this parameter is not calculated…

## Slide 54
Fin Normal Force Coefficient and CP Position
Normal Force Coefficient of the Body Tube = (CN)F
R
(CN)F = 1 + -------- x -------------------------------------
S + R
S 2
4N ---------
d
2 LF 2
1 + 1 + --------------
CR + CT

## Slide 55
Fin Normal Force Coefficient and CP Position
Location of Normal Force Coefficient of the Transition = XF
XR ( CR + 2CT ) 1 ( CR x CT )
XF = XB + ----------------------- + ----- (CR + CT ) - -------------------
3 ( CR + CT ) 6 ( CR + CT )

## Slide 56
Calculating the total CP Position
Sum the Normal Force Coefficients:
(CN)R = (CN)N + (CN)T + (CN)F
Find the CP distance from the nose tip:
(CN)N XN + (CN)T XT + (CN)F XF
XCP = ----------------------------------------------------
(CN)R
These are essentially the “moments” resulting from the lift being generated by the three primary rocket components. We don’t have to go as far as calculating the lift since the associated terms simply cancel out.

## Slide 57: Summary
The static margin is the distance between the CP and CG
The CG needs to be forward of the CP in order to have a stable rocket
  Ideally the CG should be 2 body diameters in front of the CP
Fins at the back of the rocket will move the CP aft
  Makes the rocket more stable
Larger fins tend to make the rocket more stable
  But, larger fins create more drag, which leads to lower acceleration, which leads to lower altitude

## Slide 58: Summary
Adding weight to the front of the rocket will move the CG forward
  Makes the rocket more stable
  But Newton says the rocket will not accelerate as well
Higher stability tends to make the rocket more wind sensitive

## Slide 59
Questions?