## Slide 1
Rocket Stability
Practice Problems
4 in
20 in
30 in
33 in
0.4 lb
0.2 lb
1.0 lb
LabRat Scientific
© 2018

## Slide 2
Calculate the Center of Gravity (balance point) of the following system.
10.0 N
3.0 N
5.5 N
3.5 m
2.0 m

## Slide 3
Next we calculate the moments generated by each weight.
MomentA = 5.5 N * 3.5 m = 19.25 N*m
MomentB = 3.0 N * 2.0 m = 6.0 N*m
MomentC = 10.0 N * 0.0 m = 0.0 N*m
Note: This weight does not generate a moment about the left end
Next we sum the moments:
∑Moments = 19.25 N*m + 6.0 N*m + 0.0 N*m
∑Moments = 25.25 N*m
The first step is to select a reference point so that the moments can be calculated. Lets pick the left end of the beam.

## Slide 4
We then sum the masses (or actually the weights):
∑Mass = 5.5 N + 3.0 N + 10.0 N
∑Mass = 18.5 N
Finally, we divide the sum of the moments by the sum of the masses:
25.25 N*m
XCg = --------------- = 1.36 m
18.5 N
The center of gravity of the system is located 1.36 m from the left end of the beam.

## Slide 5
Calculate the Center of Gravity of the rocket shown below. Neglect any components that are not defined.
Fins: 100 g
Motor: 300 g
Body: 150 g
Payload: 200 g
NC: 50 g
60.0 cm
55.0 cm
30.0 cm
15.0 cm
5.0 cm

## Slide 6
As usual in these types of problems, we need to select a point about which to calculate the moments. This solution uses the nose tip of the rocket.
Next we calculate the aerodynamic moments:
MomentNose = 50.0 g * 5.0 cm = 250.0 g*cm
MomentPayload = 200.0 g * 15.0 cm = 3,000.0 g*cm
MomentBody = 150.0 g * 30.0 cm = 4,500.0 g*cm
MomentMotor = 300 g * 55.0 cm = 16,500.0 g*cm
MomentFins = 100.0 g * 60.0 cm = 6,000.0 g*cm
Because of the math process, it is not necessary to convert the grams to Newtons or cm’s to m’s. The units will ultimately work out out…

## Slide 7
Next we calculate the sum of the moments:
∑Moment = 250.0 g*cm + 3000.0 g*cm + 4,500 g*cm + 16,500 g*cm + 6,000 g/cm
= 30,250 g*cm
Next we calculate the sum of the component masses:
∑Mass = 50.0 g + 200.0 g + 150.0 g + 300.0 g + 100.0 g
= 800 g

## Slide 8
Finally, we divide the sum of the moments by the sum of the masses:
30,250 g*cm
XCg = ------------------ = 37.8 cm
800.0 g
Xcg

## Slide 9
Calculate the Center of Pressure location on the rocket.
Fin Lift: 3.0 N
NC Lift: 0.5 N
60.0 cm
5.0 cm

## Slide 10
As usual in these types of problems, we need to select a point about which to calculate the moments. This solution is uses the nose tip of the rocket.
Next we calculate the sum of the aerodynamic moments:
∑Moment = 180.0 N*m + 2.5 N*m = 182.5 N*m
Next we calculate the aerodynamic moments:
MomentFin = 3.0 N * 60.0 cm = 180.0 N*m
MomentNose = 0.5 N * 5.0 cm = 2.5 N*m

## Slide 11
Next we calculate the sum of the aerodynamic forces:
∑Forces = 3.0 N + 0.5 N = 3.5 N
Finally, we divide the sum of the moments by the sum of the forces:
182.5 N*m
XCp = --------------- = 52.1 cm
3.5 N
Xcp

## Slide 12
Calculate the Static Margin based on the XCg and XCp results from the previous problems. Is the rocket stable?

## Slide 13
The static margin is the difference between the Xcg and Xcp. The governing equation is as follows:
Static Margin = Xcp - Xcg
If the Xcp is behind the Xcg the static margin will be positive (Xcp > Xcg). If the SM is negative, the rocket if unstable. Positive SM means “stable”.
Static Margin = 52.1 cm - 37.8 cm
= 14.3 cm
Xcp
Since the SM is positive the rocket is stable. Actually very stable…
Xcp