## Slide 1
Rocket Stability
Suggested Experiments
4 in
20 in
30 in
33 in
0.4 lb
0.2 lb
1.0 lb
LabRat Scientific
© 2018

## Slide 2: Exp. 1 – Stability as a Function of Fin Location
Scientific Question
  How does the location of the fins affect the stability of a rocket?
Equipment and Materials
  Experimental rocket with several movable fin sets
  String

## Slide 3
Xcg
Maintain a constant fin area for each fin set.

## Slide 4: Exp. 1 – Stability as a Function of Fin Location
Approach
  Build the test rocket with a movable fin sets (build 3 sets using 3 different fin shapes/sizes)
  Place the fins at the rear of the rocket
  Hang the rocket from its Center of Gravity
  Perform a spin test to see if the rocket is stable
  Move the fins 1” forward
  Keep the string at the same location by adding weights to the front or back of the rocket as necessary to keep the rocket balanced
  Perform a spin test to see if the rocket is stable
  Repeat steps 5 – 7
  Repeat the experiment until the rocket becomes unstable
  Repeat the experiment for the other fin set

## Slide 5: Exp. 1 – Stability as a Function of Fin Location
Data Analysis
  Determine the fin location where the rocket becomes unstable for each fin set
  Calculate the rockets static margin for each fin set
Drawing Conclusions
  How does the fin shape affect the static margin of the rocket?

## Slide 6
Xcg
Exp. 1 – Stability as a Function of Fin Location

## Slide 7
Xcg
Exp. 1 – Stability as a Function of Fin Location
Since the fins move forward, small weights need to be added at the back to keep the rocket balanced.

## Slide 8
Xcg
Exp. 1 – Stability as a Function of Fin Location
Since the fins move forward, small weights need to be added at the back to keep the rocket balanced.

## Slide 9
Xcg
Exp. 1 – Stability as a Function of Fin Location
Since the fins move forward, small weights need to be added at the back to keep the rocket balanced.
Repeat the test for the 2nd and 3rd fin sets.

## Slide 10: Exp. 2 – Stability as Function of CG Location
Scientific Question
  How does the location of the Center of Pressure affect the stability of a rocket?
Equipment and Materials
  Experimental rocket with movable balance string
  String

## Slide 11: Exp. 2 – Stability as Function of CG Location
Approach
  Build the test rocket with replaceable fin sets (use those from Exp. 1)
  Place the fin set 1 at the rear of the rocket
  Hang the rocket from its Center of Gravity
  Perform a spin test to see if the rocket is stable
  Move the string collar 1” aft and rebalance the rocket
  Perform a spin test to see check the rocket’s stability
  Repeat steps 4-5 until the rocket become unstable
  Change the fin set and repeat the experiment
Data Analysis
  Tabulate the CP locations with respect to the fin shape
  Assess which shape of fin provides the best stability

## Slide 12: Exp. 2 – Stability as Function of CG Location
Drawing Conclusions
  Which fin set provides the best stability

## Slide 13
Exp. 2 – Stability as Function of CG Location

## Slide 14
Exp. 2 – Stability as Function of CG Location
Add weights to the back of the rocket to shift the balancing point backwards.

## Slide 15
Exp. 2 – Stability as Function of CG Location
Add weights to the back of the rocket to shift the balancing point backwards.

## Slide 16
Exp. 2 – Stability as Function of CG Location
Add weights to the back of the rocket to shift the balancing point backwards.
Repeat the test for the 2nd and 3rd fin sets.