## Slide 1
Engineering Mechanics
Spring Systems and Associated Work
LabRat Scientific
© 2019

## Slide 2
WORK is done when a FORCE is applied over some DISTANCE.
Work = Force (N) x Distance (m)
The FORCE can come from any number of sources:
Gravity
Wind
Pressure
Springs
Etc…
What is Mechanical Work

## Slide 3
WORK can be either positive or negative.
Work has Direction
WORK is positive when the force acts in the direction of the movement
Force
WORK is negative when the force acts against the direction of the movement
Force

## Slide 4
Example: If Larry is trying to allow the ball to move down the ramp in a slow, controlled manner, he must apply a force to keep it from moving too fast. As such, Larry is doing negative work on the ball…
And gravity is doing positive work…
Work has Direction

## Slide 5
Hook’s Law
Force = Spring Constant (N/m) x Distance (m)
Hook’s Law is used to calculate the force generated by the compression, extension, or bending of a “springy” object like a rubber band, spring, or flexible rod. Hook’s Law is expressed as follows:
Force = k x
Relaxed Length (Force = 0)
Compressed Distance
Compressed Distance (x)

## Slide 6
Chart: Spring Force vs. Stretch Length
| 0 | 0.1 | 0.2 | 0.3
 | 0 | 1 | 2 | 3
Determining the Spring Constant
The Spring Constant (k) can be determined by applying known forces to the spring and measuring how much the spring stretches.
If the force curve is linear, the slope of line represents the Spring Constant (k)
0.0 m
1 N
0.1 m
1 N
1 N
0.2 m

## Slide 7
Chart: Spring Force vs. Stretch Length
| 0 | 0.1 | 0.2 | 0.3
 | 0 | 1 | 2 | 3
Rise
Slope = ----------
Run
Slope = 10 N/m
Spring Constant = Slope
Determining the Spring Constant
Spring Constant (k) = 10 N/m
2.0 N
Slope = ----------
0.2 m

## Slide 8
Chart: Spring Force vs. Stretch Length
| 0 | 0.1 | 0.2 | 0.3
 | 0 | 1 | 2 | 3
Work Done by a Spring
The Area under the Force Curve represents the Potential Energy of the spring.
Work is the Change in Energy of the system.
Energy is an objects “potential to do work”.
This means that the area under the Force Curve also represents the Work that is done when the spring is released.
Area = Work

## Slide 9
Chart: Spring Force vs. Stretch Length
| 0 | 0.1 | 0.2 | 0.3
 | 0 | 1 | 2 | 3
Work Done by a Spring
Area = Potential Energy
= Work
Potential Energy = Work that can
be done
PE = ½ x Base x Height
PE = ½ x 0.3 m x 3.0 N
PE = 0.45 Nm

## Slide 10
Spring Pull Experiment
0.0 m stretch
0.1 m stretch
SPRING | 
Stretch | Force
(m) | (N)
0 | 0
0.01 | 1.2
0.02 | 2.3
0.03 | 3.5
0.04 | 4.7
0.05 | 5.9
0.06 | 6.9
0.07 | 7.9
0.08 | 9.1
0.09 | 10.2
0.1 | 11.5

## Slide 11
Spring Pull Experiment
From the data we can see the force is linear as the spring is stretched
Notice how the Spring Constant curve is horizontal indicating the spring constant is constant.
Chart: Extension Spring (k)
| 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1
 | 120 | 115 | 116.6667 | 117.5 | 118 | 115 | 112.8571 | 113.75 | 113.3333 | 115
Chart: Extension Spring (Force)
| 0 | 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1
 | 0 | 1.2 | 2.3 | 3.5 | 4.7 | 5.9 | 6.9 | 7.9 | 9.1 | 10.2 | 11.5
k = 115 N/m
Slope = 11.5 N / 0.1 m
= 115 N/m

## Slide 12
Experimenters Beware…
When attempting to measure the spring force you should apply a small “preload” to the spring to get it to stretch a little before making measurements. This initial stretch eliminates any “mechanical slack” that might create an undesirable bias in the force data. This “preload force” needs to be subtracted from all the force measurements before the data is plotted. Preloading does not corrupt the spring constant calculations…
Chart: Bungie (Force)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6
 | 10 | 12 | 14 | 15 | 16.5 | 18 | 22 | 26 | 30 | 35 | 40
Here is some data from a test on a bungie cord. The cord was not pre-loaded before data was collected. You can see the bias that makes the force curve not pass through the origin (0.0 distance and 0.0 force).

## Slide 13
Rubber Band Spring
In this experiment, we will measure the force-distance of the rubber band to determine the Potential Energy.
Applied Force
Cart Motion
Experimental Verification
The Potential Energy is the amount of work that can be applied to the cart when the rubber band is released.
The work the rubber band does on the cart will make the cart move creating Kinetic Energy.

## Slide 14
The rubber band was pulled using a load cell. The force-distance data that was collected is as follows:
Actual Test Data
Experimental Verification

## Slide 15
Chart: Rubber Band Force
| 0 | 0.02 | 0.04 | 0.06 | 0.08 | 0.1
 | 0 | 0.8 | 1.7 | 2.75 | 3.8 | 5.25
The slope of the line (top of the triangle) represents the spring constant.
The measured data was not quite linear,
Area = ½ x Base x Height
Area = ½ x 0.1 m x 5 N
Area = 0.25 N*m
WorkRubber Band = 0.25 N*m
The area under the curve is the Potential Energy and the amount of work that the rubber band can do if it is released.
Experimental Verification
The measured data was not quite linear, but it was straight enough so the area could be approximated using a simple right triangle.

## Slide 16
Potential Energy = Work that can be done
Theoretical Computations
Mathematically speaking:
Work = Kinetic EnergyFinal - Kinetic EnergyInitial
When the rubber band is released it can start performing work on the cart. As work is performed, the cart is accelerated and as the cart accelerates its kinetic energy increases.
The Work-Energy Theorem states:
The change in kinetic energy of a system is equal to the amount of work done on that object.

## Slide 17
Vel = ( 2 x 0.25 N*m ) / 0.40 kg
Theoretical Computations
Vel = 1.12 m/sec
Algebra can be applied to the Work-Energy Equation to determine the theoretical velocity of the cart just when the rubber band becomes fully relaxed (Force=0):
Vel = ( 2 x Work ) / Mass
If the object is initially at rest, the Work-Energy Equation becomes:
Work = Kinetic EnergyFinal = ½ Mass x Velocity2

## Slide 18
Rubber Band fully stretched (10 cm)
Force = 5.25 N
Cart Released
Force = 0 N

## Slide 19
A ultrasonic motion sensor was used to measure the velocity as a function of time during the test.
Alternate Data Collection Method: A ruler could have been placed along the track and then video frames could be counted to obtain velocity data…
Experimental Results

## Slide 20
 | Cart Velocity
Theoretical | 1.12
Measured | 1.05
The variation between the theoretical result and the experimental result is about 5%. This is reasonable since the system is certainly not an “ideal” situation.
Experimental Results

## Slide 21
This series of experiments verify the governing equations for simple spring systems. The equations allow engineers to predict associated forces and kinetic responses to work being done on an object.

## Slide 22
Questions ?